## Slide 1
New Component Defect Detection Using Deep Learning and Gaussian Processes in Industrial Applications with Uncertainty Estimation
For oral defense
Reporter：陳昱廷
Date：2023/09/25

## Slide 2
CONTENTS
01
Related works
Qualitative analysis and Quantitative analysis
Ablation study
Introduction and
The proposed method
02
03
04
Conclusion
05
Page 4 ~ Page 22
Page 23 ~ Page 27
Page 28 ~ Page 56
Page 57 ~ Page 75
Page 76 ~ Page 78

## Slide 3
Introduction and
The proposed method
PART ONE

## Slide 4
Challenge
To improve the existing Hybrid Expert model, we need to tackle several challenges, including the complexity of the training process, the model's speed, and enhancing its overall performance.
Goal
Our goal is to improve the architecture of the previously proposed Hybrid Expert in our laboratory.
Part1: Introduction and The proposed method
Solution
The approach involves substituting the Gaussian mixture model with a Gaussian Process classifier.

## Slide 5
Part1: Introduction and The proposed method
Component visually dissimilar
Figure 1.1. Appearance of old and new components
Old component
Good
Bad
New component
Good
Bad
 | Normal sample | Defect sample
Old Component | Many | Many
New component | Many | Few or None
Table 1.1: Definition of New and Old Components

## Slide 6
Feature Extractor
Discriminative Model
Shared mbedding
Prediction
Combiner
Prediction
Converter
)
Feature extractor : MobileNetV3 Large Backbone (Pre-training on ImageNet) for feature extraction. (Output: )
: a fully connected layer with 512 output dimension. (Output:
Embedding feature : is extracted from for the training or inference of .
Discriminative Model: a fully connected layer with 2 output dimension for good and bad classification.
: a Gaussian mixture model for component classification.
Prediction Converter: analyze the output from for good, bad, unknown classification.
Prediction Combiner : combine the prediction result from and and yield the final prediction.
{‘good’, ‘bad’}, {‘good’, ‘bad’, ‘unknown’}
{‘good’, ‘bad’, ‘unknown’}
Part1: Introduction and The proposed method - Previously proposed Hybrid Expert
{}

## Slide 7
Part1: Introduction and The proposed method - Training methods for the Previously proposed Hybrid Expert
{ Good , Bad/Missing , Bad/Stand, Bad/Short, Bad/Broke, Bad/Shift }
{Good , Bad/Missing , Bad/Stand}
Feature Extractor
Cross Entropy Loss
Multi-similarity Loss
M
Stage 1
Stage 2
Shared Encoder
Feature Extractor
Shared Encoder
Shared weight
Feature Extractor
Shared Encoder

## Slide 8
Part1: Introduction and The proposed method - From Previously proposed Hybrid Expert to The Proposed Method
Gaussian Process classifier
(with K*50 inducing point)
ties to
prediction
Uncertainty
Converter
prediction
Uncertainty
to defect
converter
Feature Extractor
Prediction
Combiner
MLP classifier
Feature Extractor
Discriminative Model
Shared mbedding
Prediction
Combiner
Prediction
Converter
)
Previously proposed Hybrid Expert
Our method

## Slide 9
Part1: Introduction and The proposed method - Contribution of this study
We have achieved the following changes by transitioning from GMM to Gaussian Process classifier (GPC) :
Gaussian Processes for Large-Scale Data : To perform Gaussian process calculations on a large volume of data, we employed the optimization techniques of Inducing Points and Variational Evidence Lower Bound (ELBO).
  Inducing Points involve selecting a small subset of data points from the original dataset. These points are then used to approximate the original Gaussian process model, reducing computational complexity.
  The Variational ELBO method introduces an approximate distribution (also known as a variational distribution) using inducing points in the Gaussian process. By adjusting the positions of the inducing points, this method optimizes the approximate distribution, maximizing the variation ELBO.
Prediction uncertainty to defect detection converter : We devised this approach by implementing two predefined thresholds, and . This enables us to convert the output of the component classifier into definitive classifications of good, bad, or unknown defect states.
Spectral Normalization : By employing Spectral Normalization, we can ensure that the distances between each feature point are maintained appropriately. This method has an impact on our predictions for new components. If Spectral Normalization is not applied, our algorithm's predictions for new components would be inaccurate.

## Slide 10
Part1: Introduction and The proposed method - Our method
Feature extractor : MobileNetV3 Large Backbone (Pre-training on ImageNet) for feature extraction. (Output: )
Embedding feature : is extracted from for the training or inference of α, β.
MLP classifier : a fully connected layer with 2 output dimension for good and bad classification.
Gaussian Process classifier : Gaussian Process classifier (GPC) for Component classification.
Prediction Uncertainty to defect converter: analyze the output for good, bad, unknown classification
Prediction Combiner : combine the prediction result from and and yield the final prediction.
Output of SoftMax : prediction ty vector .
K : number of component types
Gaussian Process classifier
(with K*50 inducing point)
ties to
prediction
Uncertainty
Converter
prediction
Uncertainty
to defect
converter
Feature Extractor
Prediction
Combiner
MLP classifier
{‘good’, ‘bad’}
{‘good’, ‘bad’, ‘unknown’}
{‘good’, ‘bad’, ‘unknown’}

## Slide 11
Part1: Introduction and The proposed method - Gaussian Process classifier
Hybrid Expert
ties to
prediction
Uncertainty
Converter
Prediction
Uncertainty
to defect
converter
Feature Extractor
Prediction
Combiner
MLP classifier
Gaussian Process classifier
(with K*50 inducing point)
We implemented the component classifier via the Deterministic Uncertainty Estimation (DUE) method, which increases the capacity of a neural network with Gaussian Process classifier(GPC) methodologies.
In this context, is derived through the application of softmax likelihood to the Multivariate Normal Distribution.
During the first stage of the Gaussian Process classifier, we used the same number of inducing points as the number of classes (K). In the second stage, we froze the feature extraction and increased the number of inducing points to K*50.
Notes: 我們通過確定性不確定性估計（DUE）方法實現了component分類器，該方法通過高斯過程分類器（GPC）方法增加了神經網絡的能力。
在這種情況下，{是通過將 softmax likelihood 應用於多元正態分佈(Multivariate Normal Distribution)而得出的。
在高斯過程分類器的第一階段，我們使用與類別數量 (K) 相同數量的 inducing points 。 在第二階段，我們凍結特徵提取並將inducing points數量增加到K*50。
我們通過確定性不確定性估計（DUE）方法實現了component分類器，該方法通過高斯過程分類器（GPC）方法增加了神經網絡的能力。
在這種情況下，{y ̂_com}是通過將 softmax likelihood 應用於多元正態分佈(Multivariate Normal Distribution)而得出的。
在高斯過程分類器的第一階段，我們使用與類別數量 (K) 相同數量的 inducing points 。 在第二階段，我們凍結特徵提取並將inducing points數量增加到K*50。

## Slide 12
Part1: Introduction and The proposed method - Probabilities to prediction Uncertainty Converter
Hybrid Expert
ties to
prediction
Uncertainty
Converter
Prediction
Uncertainty
to defect
converter
Feature Extractor
Prediction
Combiner
MLP classifier
Gaussian Process classifier
(with K*50 inducing point)
The “Probabilities to prediction Uncertainty Converter” is designed to calculate Uncertainty using the probabilities of belonging to each component class.
In this context, we utilize Entropy to compute Normalized Uncertainty:

## Slide 13
Part1: Introduction and The proposed method - Prediction Uncertainty to defect converter
Hybrid Expert
ties to
prediction
Uncertainty
Converter
Prediction
Uncertainty
to defect
converter
Feature Extractor
Prediction
Combiner
MLP classifier
Gaussian Process classifier
(with K*50 inducing point)
Through the implementation of two predefined thresholds : ,we can transform the output of the component classifier into definitive classifications of good, bad, or unknown defect states.
0
good
bad
unknown
1
Normalized Uncertainty (U)

## Slide 14
Part1: Introduction and The proposed method - Algorithm for Prediction Uncertainty to defect converter
K : number of component types
{1, 2, 3, ,K} is the name of training component
Prediction Uncertainty to defect converter:
  If ( U >):
  = Unknown
  If ( ):
  = Bad
  If ( ):
  = Good
Normalized Uncertainty
0
good
bad
unknown
1
In our study, we set that when uncertainty is less than , the prediction is considered "good," when uncertainty falls between and , it is categorized as "bad," and when uncertainty is greater than , it is classified as "unknown.“
Find the , that produces the best performance by observing the variation of the overkill rate, leakage rate, and unknown rate in the training and validation sets.
, optimized by Bayesian optimizer , find the best average of Overkill rate, Leakage rate, Unknown rate.

## Slide 15
Inducing points = number of component types * 50
{ Good , Bad/Missing , Bad/Stand, Bad/Short, Bad/Broke, Bad/Shift }
{Good , Bad/Missing , Bad/Stand}
Feature Extractor
Cross Entropy Loss
Variational
ELBO
Stage 1
Feature Extractor
Stage 2
Variational
ELBO
Part1: Introduction and The proposed method - Training procedure of our method
Feature Extractor
Shared weight
Inducing points = number of component types
The main focus of this study is that, unlike the research on DUE, we achieve better results by freezing the parameters of the feature extractor after training in stage 1 and then using more inducing points for further training.

## Slide 16
Part 1: Introduction and The proposed method - 2D schematic diagram derived from test samples of the new component.
Gaussian Process classifier
(with K*50 inducing point)
ties to
prediction
Uncertainty
Converter
prediction
Uncertainty
to defect
converter
Feature Extractor
Prediction
Combiner
MLP classifier
Upper branch
(Defect detection)
Uncertainty
low
high
Expert 1 : use only the upper branch
Good samples of new component.
Bad samples of new component.
It can be observed that when only the upper branch is utilized, the new component tends to exhibit confusion between good and bad samples, resulting in incorrect predictions.
Expert 1 has already exhibit very good accuracy for old components.
Notes: In (a) Expert 1, the bad test samples overlap with the good test samples. In addition, missing and stand islands are mixed in the feature space
In (b) Expert 2, missing and stand islands are not mixed in the feature space.
The missing and stand islands are separated in (c) Hybrid Expert.
Furthermore, the bad test samples are push away from the good test samples as illustrated in (c) Hybrid Expert.

## Slide 17
Part 1: Introduction and The proposed method - 2D schematic diagram derived from test samples of the new component.
Gaussian Process classifier
(with K*50 inducing point)
ties to
prediction
Uncertainty
Converter
prediction
Uncertainty
to defect
converter
Feature Extractor
Prediction
Combiner
MLP classifier
(b) Lower branch
(Component classification)
Uncertainty
low
high
Expert 2 : use only the lower branch
Good samples of new components.
Bad samples of new components.
The lower branch consists of a modified DUE and newly designed prediction converters.
When exclusively utilizing the lower branch, it becomes apparent that the new component tends to confuse between good and bad samples, leading to inaccurate predictions.
Notes: In (a) Expert 1, the bad test samples overlap with the good test samples. In addition, missing and stand islands are mixed in the feature space
In (b) Expert 2, missing and stand islands are not mixed in the feature space.
The missing and stand islands are separated in (c) Hybrid Expert.
Furthermore, the bad test samples are push away from the good test samples as illustrated in (c) Hybrid Expert.

## Slide 18
Part 1: Introduction and The proposed method - 2D schematic diagram derived from test samples of the new component.
ties to
prediction
Uncertainty
Converter
prediction
Uncertainty
to defect
converter
Feature Extractor
Prediction
Combiner
MLP classifier
(c) Hybrid Expert
Uncertainty
low
high
Hybrid Expert : Base on DUE
Gaussian Process classifier
(with K*50 inducing point)
Good samples of new component.
Bad samples of new component.
Bad and good samples of the three new components are well separated.
Notes: In (a) Expert 1, the bad test samples overlap with the good test samples. In addition, missing and stand islands are mixed in the feature space
In (b) Expert 2, missing and stand islands are not mixed in the feature space.
The missing and stand islands are separated in (c) Hybrid Expert.
Furthermore, the bad test samples are push away from the good test samples as illustrated in (c) Hybrid Expert.

## Slide 19
Part 1: Introduction and The proposed method - Hypothesis on the Relationship Between Sample Uncertainty and Position in t-SNE
Hybrid Expert
Uncertainty
low
high
Good samples of new component.
Bad samples of new component.
In our study, we formulated a hypothesis that uncertainty is lowest on the island, slightly higher at the island's edges, and increases as one moves farther away from the island. Subsequent experiments have provided evidence supporting the validity of this hypothesis.
Notes: In (a) Expert 1, the bad test samples overlap with the good test samples. In addition, missing and stand islands are mixed in the feature space
In (b) Expert 2, missing and stand islands are not mixed in the feature space.
The missing and stand islands are separated in (c) Hybrid Expert.
Furthermore, the bad test samples are push away from the good test samples as illustrated in (c) Hybrid Expert.

## Slide 20
low
high
(1) With spectral normalization
Uncertainty
(2) Without spectral normalization
If spectral normalization is not used, a greater separation between the positive and negative samples will occur. When applying Bayesian optimization, this results in an increase in .
While there is no impact on predicting the old component, a higher unknown rate is observed when predicting the new component.
Part 1: Introduction and The proposed method - Effect of spectral normalization
Notes: T-sne : P95

## Slide 21
Model | With spectral normalization | Without spectral normalization
Advantages | The new component bad samples can be pushed to the edge of the island rather than being pushed further into the sea. As a result, the "unknown" instances in the lower branch of the Hybrid Expert will be lower. | The model's reasoning ability is stronger, and it will push the bad samples far away from the islands of each element. As a result, there is less likelihood of misjudgment, and overkill and leakage will be lower.
Disadvantages | The model's reasoning ability will be constrained by the SN . Consequently, the bad samples will be pushed around the islands, which will also lead to a higher likelihood of misjudgment, overkill, and leakage. | Due to its stronger capabilities, the model might push the bad samples of the new component into the sea, which would result in a higher number of "unknown" instances in the lower branch of the Hybrid Expert.
properties | The performance of the new component is expected to be better . | The performance of the new component is expected to be worse .
Part 1: Introduction and The proposed method - Effect of spectral normalization

## Slide 22
Part1: Introduction and The proposed method - Summary
We propose a Hybrid Expert which is a combination of MLP classifier (Defect detector branch) and Gaussian Process classifier (Component Classifier branch).
Outperformance of Previous Approach:
Calibrated Score was improved from 0.98728 to 0.99173. For 8-fruit dataset, from 0.9317 to 0.95064.
Enhanced training speed:
  Previously proposed Hybrid Expert : Around 8.57 hours ± 1.36 hours (with Bayesian optimization 50 iterations taking "16.86 hours ± 0.9 hours").
  Our method: Only 6.834 hours ± 2.21 hours (with Bayesian optimization 200 iterations taking "15.81 hours ± 1.79 hours").
Improved inference Speed:
  Previously proposed Hybrid Expert’s detection time: "25.51 minutes ± 3.66 minutes".
  Our method’s detection time: "5.947 minutes ± 2.229 minutes".

## Slide 23
Related works
PART TWO

## Slide 24
Part2: Related works - Gaussian Process Classifier
Gaussian Process classifiers have advantages in handling uncertainty and Kernel function optimization, making them efficient and flexible machine learning methods.
The Gaussian Process classifier is based on interpolation, predicting the labels of new data points by interpolating between the training data points.
Gaussian Process classifier can estimate predictive uncertainty, indicating the model's confidence in its predictions.
Use Gaussian Process (GP) to define uncertainty allows for easier algebraic computations and improves model efficiency.
The Kernel function is crucial for the GP classifier as it measures the similarity between data points.
Optimizing the parameters of the Kernel function is an important step to adjust the model's performance.
Notes: GP 分類器基於內插，通過訓練數據點之間的插值來預測新數據點的標籤。
GP 分類器能夠估計預測的不確定性，告訴我們模型對預測的信心程度。
選擇使用高斯過程 (GP) 定義不確定性，容易進行代數運算，提高模型效率。
核函數 (Kernel) 是 GP 分類器的關鍵，用於衡量數據點之間的相似性。
優化核函數的參數是調整模型性能的重要步驟，需要根據問題需求選擇合適的核函數及其參數。
Gaussian Process 分類器在處理不確定性和優化核函數方面具有優勢，是一種高效且靈活的機器學習方法

## Slide 25
(a) ResNet + Softmax
(b) DUE
[2] van Amersfoort, J., Smith, L., Jesson, A., Key, O., & Gal, Y. (2021). On feature collapse and deep kernel learning for single forward pass uncertainty. arXiv preprint arXiv:2102.11409.
DUE combines the strengths of both deep learning and kernel methods, it can be used to make predictions with uncertainty.
Thus, we can estimate the uncertainty of a test sample based on its entropy and then filter out the unknown samples.
Part2: Related works - Deterministic Uncertainty Estimation
 | DUE | Our method
Goal | By computing uncertainty, it is possible to identify which samples are Out-of-Distribution (Unknown). | By calculating uncertainty ,it is not only possible to identify unknown samples but also perform defect detection.
Characteristics | The Bayesian properties of the Gaussian process model were utilized to estimate uncertainties effectively. | The Bayesian properties of the Gaussian process model were utilized to estimate uncertainties effectively.
Model Setting | Using only the same number of inducing points as the category. | Using the same number of inducing points as the category in stage 1 and freezing the feature extractor's parameters, we employ additional inducing points for further training.

## Slide 26
Model | GMM | DUE
Characteristics | A generative model that assumes data comes from a mixture of multiple Gaussian distributions. | A non-parametric model that learns correlation between data through a kernel function.
Goal | To model observed data. | To make predictions and uncertainty estimation for new data.
Advantages | The model has higher interpretability. | The DUE method allows for error feedback during the fitting process.
Disadvantages | During training, GMM is unable to provide error feedback to the feature extractor. | The model has a lower interpretability.
Part2: Related works - Deterministic Uncertainty Estimation(DUE) vs Gaussian Mixture Model (GMM)

## Slide 27
Part2: Related works - Compositional Zero-shot Learning
[1] Karthik, S., Mancini, M., & Akata, Z. (2022). KG-SP: Knowledge Guided Simple Primitives for Open World Compositional Zero-Shot Learning. In Proceedings of the IEEE/CVF Conference on Computer Vision and Pattern Recognition (pp. 9336-9345).
The goal of compositional zero-shot learning (CZSL) is to recognize compositions composed of a set of states and objects. (e.g., red apple, where red is the state and apple is the object). Their architecture is similar to ours, but there are some differences.
 | CZSL | previously proposed Hybrid Expert | Our method
Goal | To predict state and object | To predict defect type | To predict defect type
Purpose of each branch | One is to predict state and another one is to predict object | The upper branch performs defect detection.; the lower branch predicts component type, and then transform the prediction to defect detection. | The upper branch performs defect detection.; the lower branch predicts component type, and then transform the prediction to defect detection.
Unknown-aware prediction | X | ✔ | ✔
Table 1.1. Difference between CZSL and our task.
Idea of compositional zero-shot learning, image is retrieved from [1].
Notes: Defect = state , component = object
CZSL : predict state and object
Ours : predict defect
可以將只判斷good bad , 或是判斷不同defect type

## Slide 28
Qualitative analysis and Quantitative analysis
PART THREE

## Slide 29
Part3: Qualitative analysis and Quantitative analysis - Experiment Setup
Framework | PyTorch | 
Backbone | MobileNet V3 Large, pre-trained on ImageNet | 
Image size | 3 224 224 ( channel height width) | 
Epoch | 50 | 
Batch size | 128 | 
Learning rate | decay the learning rate at epoch 20, 30, 40 | 
Optimizer | Two independent SGD optimizer were used for updating model parameter. (a) feature extractor , defect detector . (b) feature extractor , component classifier . | 
Data Augmentation | Training set Random horizontal flip, random vertical flip, color jitter, and random gray scale | Validation set and test set No augmentation
GPU | A single NVIDIA Tesla V100 GPU for each experiment | 
Framework | PyTorch | 
Backbone | MobileNet V3 Large, pre-trained on ImageNet | 
Image size |  | 
Epoch | 50 | 
Batch size | 128 | 
Learning rate |  | 
Optimizer |  | 
Data Augmentation | Training set Random horizontal flip, random vertical flip, color jitter, and random gray scale | Validation set and test set No augmentation
GPU | A single NVIDIA Tesla V100 GPU for each experiment | 
Table 3.1. Summary for the experiment setup.

## Slide 30
Part3: Qualitative analysis and Quantitative analysis - t-sne visualization of z from train and test samples
Background : Training set
Foreground : Test set (Red circle and Green Cross )
Upper branch
(Defect detection)
Expert 1 : use only the upper branch
Gaussian Process classifier
(with K*50 inducing point)
ties to
prediction
Uncertainty
Converter
prediction
Uncertainty
to defect
converter
Feature Extractor
Prediction
Combiner
MLP classifier
It can be observed that when only the upper branch is utilized, the new component tends to exhibit confusion between good and bad samples, resulting in incorrect predictions.
Note that both good and bad samples of the training set(old and new component) are shown in the background.
both good and bad samples of the test set (old and new component) are shown in the foreground.
Notes: In (a) Expert 1, the bad test samples overlap with the good test samples. In addition, missing and stand islands are mixed in the feature space
In (b) Expert 2, missing and stand islands are not mixed in the feature space.
The missing and stand islands are separated in (c) Hybrid Expert.
Furthermore, the bad test samples are push away from the good test samples as illustrated in (c) Hybrid Expert.

## Slide 31
Part3: Qualitative analysis and Quantitative analysis - t-sne visualization of z from train and test samples
Background : Training set
Foreground : Test set (Red circle and Green Cross )
Expert 2 : use only the lower branch
(b) Lower branch
(Component classification)
The lower branch consists of a modified DUE and newly designed prediction converters.
Gaussian Process classifier
(with K*50 inducing point)
ties to
prediction
Uncertainty
Converter
prediction
Uncertainty
to defect
converter
Feature Extractor
Prediction
Combiner
MLP classifier
When exclusively utilizing the lower branch, it becomes apparent that the new component tends to confuse between good and bad samples, leading to inaccurate predictions.
Note that only good samples of the training set(old and new component) are shown in the background.
both good and bad samples of the test set (old and new component) are shown in the foreground.
Notes: In (a) Expert 1, the bad test samples overlap with the good test samples. In addition, missing and stand islands are mixed in the feature space
In (b) Expert 2, missing and stand islands are not mixed in the feature space.
The missing and stand islands are separated in (c) Hybrid Expert.
Furthermore, the bad test samples are push away from the good test samples as illustrated in (c) Hybrid Expert.

## Slide 32
Part3: Qualitative analysis and Quantitative analysis - t-sne visualization of z from train and test samples
Background : Training set
Foreground : Test set (Red circle and Green Cross )
(c) Hybrid Expert
Hybrid Expert : Base on DUE
The Hybrid Expert architecture is built upon the foundation of the DUE with significant improvements.
ties to
prediction
Uncertainty
Converter
prediction
Uncertainty
to defect
converter
Feature Extractor
Prediction
Combiner
MLP classifier
Gaussian Process classifier
(with K*50 inducing point)
Note that only good samples of the training set(old and new component) are shown in the background.
both good and bad samples of the test set (old and new component) are shown in the foreground.
Notes: In (a) Expert 1, the bad test samples overlap with the good test samples. In addition, missing and stand islands are mixed in the feature space
In (b) Expert 2, missing and stand islands are not mixed in the feature space.
The missing and stand islands are separated in (c) Hybrid Expert.
Furthermore, the bad test samples are push away from the good test samples as illustrated in (c) Hybrid Expert.

## Slide 33
Part3: Qualitative analysis and Quantitative analysis - Evaluation Metrics
The number of false positive samples divided by the total number of test samples .
The number of false negative samples divided by the total number of test samples.
The number of test samples predicted to be unknown divided by the total number of test samples .

## Slide 34
Score =
Part3: Qualitative analysis and Quantitative analysis - Evaluation Metrics
The exp() function is an exponential function used to address the issue of encountering 0 in the Overkill rate, Leakage rate, and Unknown rate variables. Its purpose is to prevent the formula from being unable to calculate due to a denominator of 0.
In general, we set , , and to 1 and use Bayesian optimization to find , , and we can adjust the parameters of 𝑎, 𝑏, and 𝑐 according to our needs.
Score =

## Slide 35
Comparison between Previously Proposed Hybrid Expert Method and Our Approach:
We will compare the previously proposed hybrid expert method with our newly introduced approach.
This comparison will help us determine whether our method outperforms the previously proposed hybrid expert method.
Part3: Qualitative analysis and Quantitative analysis - Comparison between Previously Proposed Hybrid Expert Method and Our Approach

## Slide 36
Method | Overkill rate | Leakage rate | Unknown rate | Overkill + Leakage rate | Score
Previously proposed Hybrid Expert | 0.108% ± 0.033% | 0.063% ± 0.075% | 3.706% ± 2.270% | 0.171% ± 0.108% | 0.9873
Our Method | 0.027% ± 0.02% | 0.131% ± 0.059% | 2.237% ± 0.93% | 0.158% ± 0.049% | 0.9921
Part3: Qualitative analysis and Quantitative analysis - Comparison between Previously Proposed Hybrid Expert Method and Our Approach
The experimental results, averaged over three different dataset splits, utilized all components (old + new components).
The introduction of the dataset can be found on page 85.
Overkill, Leakage and Unknown rate on Phison PCB datasets
From the following content, it can be seen that the previously proposed Hybrid Expert had a score of 0.9873, while our method improved it to 0.9921.

## Slide 37
Method | Calibrated Overkill rate | Calibrated Leakage rate | Unknown rate | Calibrated Overkill + Leakage rate | Calibrated Score
Previously proposed Hybrid Expert | 0.112% ± 0.035% | 0.065% ± 0.078% | 3.706% ± 2.270% | 0.178% ± 0.113% | 0.98728
Our Method | 0.027% ± 0.02% | 0.134% ± 0.06% | 2.237% ± 0.93% | 0.161% ± 0.048% | 0.99209
Part3: Qualitative analysis and Quantitative analysis - Comparison between Previously Proposed Hybrid Expert Method and Our Approach
The experimental results, averaged over three different dataset splits, utilized all components (old + new components).
The introduction of the dataset can be found on page 85.
Calibrated Overkill, Leakage and Unknown rate on Phison PCB datasets
From the following content, it can be seen that the previously proposed Hybrid Expert had a Calibrated score of 0.98728, while our method improved it to 0.99209.

## Slide 38
Part3: Qualitative analysis and Quantitative analysis - Effect of Changing the weighting parameters of Harmonic mean in Our Method
Comparing the weighting parameters of the Harmonic mean to assess the effectiveness of Bayesian optimization:
From the experimental results on the previous page, we observed a higher leakage in our approach.
To address this issue, we sought to find the optimal leakage rate by modifying the weighting parameters of the Harmonic mean and utilizing Bayesian optimization.

## Slide 39
Use Bayesian optimization to find ,
Change the weighting parameters of 𝐻𝑎𝑟𝑚𝑜𝑛𝑖𝑐 𝑚𝑒𝑎𝑛 to find the best Leakage rate ( e.g. (a, b, c ) = (1, 50, 1) )
Method | Overkill rate | Leakage rate | Calibrated Overkill rate | Calibrated Leakage rate | Unknown rate
Hybrid Expert (weighting parameters of 𝐻𝑎𝑟𝑚𝑜𝑛𝑖𝑐 𝑚𝑒𝑎𝑛 (a, b, c ) = (1, 1, 1) ) | 0.027% ± 0.02% | 0.131% ± 0.059% | 0.027% ± 0.02% | 0.134% ± 0.06% | 2.237% ± 0.93%
Hybrid Expert (weighting parameters of 𝐻𝑎𝑟𝑚𝑜𝑛𝑖𝑐 𝑚𝑒𝑎𝑛 (a, b, c ) = (1, 50, 1) ) | 0.276% ± 0.331% | 0.081% ± 0.039% | 0.284% ± 0.341% | 0.083 ± 0.04% | 2.544% ± 0.36%
The experimental results, averaged over three different dataset splits, utilized all components (old + new components).
The introduction of the dataset can be found on page 85.
Part3: Qualitative analysis and Quantitative analysis - Effect of Changing the weighting parameters of Harmonic mean in Our Method
From the following content, it can be seen that by changing the weighting parameters of Harmonic mean, the Calibrated Leakage rate decreased from 0.134% ± 0.06% to 0.083% ± 0.04%.

## Slide 40
Use Bayesian optimization to find ,
Change the weighting parameters of 𝐻𝑎𝑟𝑚𝑜𝑛𝑖𝑐 𝑚𝑒𝑎𝑛 to find the best Leakage rate ( e.g. (a, b, c ) = (50, 50, 1) )
Method | Overkill rate | Leakage rate | Calibrated Overkill rate | Calibrated Leakage rate | Unknown rate
Hybrid Expert (weighting parameters of 𝐻𝑎𝑟𝑚𝑜𝑛𝑖𝑐 𝑚𝑒𝑎𝑛 (a, b, c ) = (1, 1, 1) ) | 0.027% ± 0.02% | 0.131% ± 0.059% | 0.027% ± 0.02% | 0.134% ± 0.06% | 2.237% ± 0.93%
Hybrid Expert (weighting parameters of 𝐻𝑎𝑟𝑚𝑜𝑛𝑖𝑐 𝑚𝑒𝑎𝑛 (a, b, c ) = (50, 50, 1) ) | 0.042% ± 0.058% | 0.112% ± 0.042% | 0.043% ± 0.059% | 0.114 ± 0.043% | 2.411% ± 0.722%
The experimental results, averaged over three different dataset splits, utilized all components (old + new components).
The introduction of the dataset can be found on page 85.
Part3: Qualitative analysis and Quantitative analysis - Effect of Changing the weighting parameters of Harmonic mean in Our Method
From the following content, it can be seen that by changing the weighting parameters (50,50,1) of Harmonic mean, the Calibrated Leakage rate decreased from 0.134% ± 0.06% to 0.114% ± 0.043%.

## Slide 41
Comparing the Performance between Expert 1, Expert 2, and Hybrid Expert :
The performance of Expert 1 and Expert 2 is separately evaluated, and their performance is compared to our hybrid expert approach. This analysis aims to gain insights into the limitations of relying solely on one of these experts.
By individually assessing the performance of Expert 1 and Expert 2 , it helps determine whether the hybrid expert approach can address the shortcomings of relying solely on one of these experts and offer a more comprehensive solution.
Part3: Qualitative analysis and Quantitative analysis - Comparing the Performance between Expert 1, Expert 2, and Hybrid Expert
Notes: 我們分別對專家 1 和專家 2 的性能進行了評估，並將它們的性能與我們的混合專家方法進行了比較。這項分析旨在深入了解僅依賴其中一位專家的局限性。
通過分別評估專家 1 和專家 2 的性能，有助於確定混合專家方法是否能解決僅依賴其中一位專家的缺點，並提供更全面的解決方案。

## Slide 42
Method | Overkill rate | Leakage rate | Unknown rate | Overkill + Leakage rate
Expert 1 | 0.079% ± 0.056% | 0.503% ± 0.278% | - | 0.581% ± 0.305%
Expert 2 | 1.244% ± 1.632% | 0.805% ± 0.214% | 1.802% ± 1.306% | 2.048% ± 1.683%
Hybrid Expert | 0.027% ± 0.02% | 0.131% ± 0.059% | 2.237% ± 0.93% | 0.158% ± 0.049%
Part3: Qualitative analysis and Quantitative analysis - Comparing the Performance between Expert 1, Expert 2, and Hybrid Expert
The experimental results, averaged over three different dataset splits, utilized all components (old + new components).
The introduction of the dataset can be found on page 85.
Overkill, Leakage and Unknown rate on Phison PCB datasets
From the table, it can be seen that Hybrid Expert performs better in terms of the “Overkill + Leakage rate” compared to Expert 1, and Expert 2.

## Slide 43
Method | Calibrated Overkill rate | Calibrated Leakage rate | Unknown rate | Calibrated Overkill + Leakage Rate
Expert 1 | 0.079% ± 0.056% | 0.503% ± 0.278% | - | 0.581% ± 0.305%
Expert 2 | 1.254% ± 1.638% | 0.819% ± 0.222% | 1.802% ± 1.306% | 2.073% ± 1.679%
Hybrid Expert | 0.027% ± 0.02% | 0.134% ± 0.06% | 2.237% ± 0.93% | 0.161% ± 0.048%
Part3: Qualitative analysis and Quantitative analysis - Comparing the Performance between Expert 1, Expert 2, and Hybrid Expert
Calibrated Overkill, Leakage and Unknown rate on Phison PCB datasets
The experimental results, averaged over three different dataset splits, utilized all components (old + new components).
The introduction of the dataset can be found on page 85.
From the table, it can be seen that Hybrid Expert performs better in terms of the “Calibrated Overkill + Leakage rate” compared to Expert 1, and Expert 2.

## Slide 44
Background : Training set
Foreground : Test set (Red circle and Green Cross )
Upper branch
(Defect detection)
Gaussian Process classifier
ties to
prediction
Uncertainty
Converter
prediction
Uncertainty
to defect
converter
Feature Extractor
Prediction
Combiner
MLP classifier
Expert 1 : use only the upper branch
Part3: Qualitative analysis and Quantitative analysis
- t-SNE visualization of z from train and test samples on other datasets – 8 fruit
Note that both good and bad samples of the training set(old and new fruit) are shown in the background.
both good and bad samples of the test set (old and new fruit) are shown in the foreground.
It can be observed that when only the upper branch is utilized, the new component tends to exhibit confusion between good and bad samples, resulting in incorrect predictions.
Notes: In (a) Expert 1, the bad test samples overlap with the good test samples. In addition, missing and stand islands are mixed in the feature space
In (b) Expert 2, missing and stand islands are not mixed in the feature space.
The missing and stand islands are separated in (c) Hybrid Expert.
Furthermore, the bad test samples are push away from the good test samples as illustrated in (c) Hybrid Expert.

## Slide 45
strawberry
jujube
Guava
Orange
Pomegranate
Apple
Banana
Grape
Background : Training set
Foreground : Test set (Red circle and Green Cross )
(b) Lower branch
(Component classification)
Gaussian Process classifier
ties to
prediction
Uncertainty
Converter
prediction
Uncertainty
to defect
converter
Feature Extractor
Prediction
Combiner
MLP classifier
Expert 1 : use only the lower branch
Part3: Qualitative analysis and Quantitative analysis
- t-SNE visualization of z from train and test samples on other datasets – 8 fruit
Note that only good samples of the training set(old and new fruit) are shown in the background.
both good and bad samples of the test set (old and new fruit) are shown in the foreground.
When exclusively utilizing the lower branch, it becomes apparent that the new component tends to confuse between good and bad samples, leading to inaccurate predictions.
Notes: In (a) Expert 1, the bad test samples overlap with the good test samples. In addition, missing and stand islands are mixed in the feature space
In (b) Expert 2, missing and stand islands are not mixed in the feature space.
The missing and stand islands are separated in (c) Hybrid Expert.
Furthermore, the bad test samples are push away from the good test samples as illustrated in (c) Hybrid Expert.

## Slide 46
Background : Training set
Foreground : Test set (Red circle and Green Cross )
Gaussian Process classifier
ties to
prediction
Uncertainty
Converter
prediction
Uncertainty
to defect
converter
Feature Extractor
Prediction
Combiner
MLP classifier
(c) Hybrid Expert
Hybrid Expert : Base on DUE
Part3: Qualitative analysis and Quantitative analysis
- t-SNE visualization of z from train and test samples on other datasets – 8 fruit
strawberry
jujube
Guava
Grape
Orange
Pomegranate
Apple
Banana
Note that only good samples of the training set(old and new fruit) are shown in the background.
both good and bad samples of the test set (old and new fruit) are shown in the foreground.
Notes: 用46頁的圖來看 test bad sample 有沒有被推開到島的旁邊 , 下面48~51頁再用兩張圖來一起看 被推開的樣本uncertainty是否符合我們的假設 , 46頁的圖與傳統的tsne 的圖比較接近 可以讓讀者比較容易了解 所以還是留下來比較好, 一開始就放uncertainty map的圖 可能會讓人看不懂

## Slide 47
Method | Overkill rate | Leakage rate | Unknown rate | Overkill + Leakage rate | Score
Previously proposed Hybrid Expert | 2.967% ± 0.124% | 0% ± 0% | 18.47% ± 10.69% | 2.967% ± 0.124% | 0.93403
Our Method | 1.187% ± 0.659% | 1.214% ± 0.797% | 12.84% ± 1.915% | 2.4% ± 1.43% | 0.95189
Part3: Qualitative analysis and Quantitative analysis - Comparison between Previously Proposed Hybrid Expert Method and Our Approach
The experimental results, averaged over three different dataset splits, utilized all fruit (old + new fruit).
The introduction of the dataset can be found on page 102.
Overkill, Leakage and Unknown rate on other datasets – 8 fruit
From the following content, it can be seen that the previously proposed Hybrid Expert had a score of 0.93403, while our method improved it to 0.95189.

## Slide 48
Method | Calibrated Overkill rate | Calibrated Leakage rate | Unknown rate | Calibrated Overkill + Leakage rate | Calibrated Score
Previously proposed Hybrid Expert | 3.689% ± 0.585% | 0% ± 0% | 18.47% ± 10.69% | 3.689% ± 0.585% | 0.9317
Our Method | 1.373% ± 0.796% | 1.406% ± 0.955% | 12.84% ± 1.915% | 2.779% ± 1.723% | 0.95064
Part3: Qualitative analysis and Quantitative analysis - Comparison between Previously Proposed Hybrid Expert Method and Our Approach
Calibrated Overkill, Leakage and Unknown rate on other datasets – 8 fruit
The experimental results, averaged over three different dataset splits, utilized all fruit (old + new fruit).
The introduction of the dataset can be found on page 102.
From the following content, it can be seen that the previously proposed Hybrid Expert had a Calibrated score of 0.9317, while our method improved it to 0.95064.

## Slide 49
Method | Overkill rate | Leakage rate | Unknown rate | Overkill + Leakage rate
Expert 1 | 1.106% ± 0.306% | 6.447% ± 2.834% | - | 7.553% ± 2.667%
Expert 2 | 3.452% ± 1.201% | 14.132% ± 2.877% | 2.158% ± 2.209% | 17.58% ± 3.491%
Hybrid Expert | 1.187% ± 0.659% | 1.214% ± 0.797% | 12.84% ± 1.915% | 2.4% ± 1.43%
Overkill, Leakage and Unknown rate on other datasets – 8 fruit
Part3: Qualitative analysis and Quantitative analysis - Comparing the Performance between Expert 1, Expert 2, and Hybrid Expert
The experimental results, averaged over three different dataset splits, utilized all fruit (old + new fruit).
The introduction of the dataset can be found on page 102.
From the table, it can be seen that Hybrid Expert performs better in terms of the “Overkill + Leakage rate” compared to Expert 1, and Expert 2.

## Slide 50
Method | Calibrated Overkill rate | Calibrated Leakage rate | Unknown rate | Calibrated Overkill + Leakage Rate
Expert 1 | 1.106% ± 0.306% | 6.447% ± 2.834% | - | 7.553% ± 2.667%
Expert 2 | 3.512% ± 1.149% | 14.42% ± 2.761% | 2.158% ± 2.209% | 17.93% ± 3.264%
Hybrid Expert | 1.373% ± 0.796% | 1.406% ± 0.955% | 12.84% ± 1.915% | 2.779% ± 1.723%
Calibrated Overkill, Leakage and Unknown rate on other datasets – 8 fruit
Part3: Qualitative analysis and Quantitative analysis - Comparing the Performance between Expert 1, Expert 2, and Hybrid Expert
The experimental results, averaged over three different dataset splits, utilized all fruit (old + new fruit).
The introduction of the dataset can be found on page 102.
From the table, it can be seen that Hybrid Expert performs better in terms of the “Calibrated Overkill + Leakage rate” compared to Expert 1, and Expert 2.

## Slide 51
Part3: Qualitative analysis and Quantitative analysis -Explanation of t-SNE Visualization Based on Uncertainty Observation
Different Directions of t-SNE Visualization Focus :
In traditional tasks, we analyze predictions by observing the distances between samples in t-SNE. However, our approach goes beyond this; we can also predict defects in samples by observing different uncertainties.
The observed results can confirm our previous hypothesis that uncertainty is lowest on the island, slightly higher at the island's edges, and increases as we move farther away from the island.
Notes: 我們分別對專家 1 和專家 2 的性能進行了評估，並將它們的性能與我們的混合專家方法進行了比較。這項分析旨在深入了解僅依賴其中一位專家的局限性。
通過分別評估專家 1 和專家 2 的性能，有助於確定混合專家方法是否能解決僅依賴其中一位專家的缺點，並提供更全面的解決方案。

## Slide 52
Part3: Qualitative analysis and Quantitative analysis - t-SNE visualization of Uncertainty – 8 fruit
strawberry
jujube
Guava
Orange
Pomegranate
Apple
Banana
New Fruit
Expert 2 (Only GP)
(With SN =3)
Grape
Uncertainty
low
high
Many of the bad samples cannot be pushed away from the islands (i.e., clusters), producing low uncertainty estimation (purple color) and leading to inaccurate predictions.
Note that only good samples of the training set(old and new fruit) are shown in the background.
both good and bad samples of the test set (new fruit) are shown in the foreground.

## Slide 53
Part3: Qualitative analysis and Quantitative analysis - t-SNE visualization of Uncertainty – 8 fruit
Old Fruit
Expert 2 (Only GP)
(With SN =3)
strawberry
jujube
Guava
Orange
Pomegranate
Apple
Banana
Grape
Uncertainty
low
high
Many of the bad samples cannot be pushed away from the islands (i.e., clusters), producing low uncertainty estimation (purple color) and leading to inaccurate predictions.
Note that only good samples of the training set(old and new fruit) are shown in the background.
both good and bad samples of the test set (old fruit) are shown in the foreground.

## Slide 54
Note that only good samples of the training set(old and new fruit) are shown in the background.
both good and bad samples of the test set (new fruit) are shown in the foreground.
Part3: Qualitative analysis and Quantitative analysis - t-SNE visualization of Uncertainty – 8 fruit
strawberry
jujube
Guava
Grape
Orange
Pomegranate
Apple
Banana
New Fruit
Hybrid Expert
(With SN =3)
Uncertainty
low
high
Purple color denotes good samples(Low uncertainty), bad samples are between the range of light blue to orange color. Samples that outside of the islands (i.e., clusters) are between orange and red. (High uncertainty)

## Slide 55
Part3: Qualitative analysis and Quantitative analysis - t-SNE visualization of Uncertainty – 8 fruit
Uncertainty
low
high
strawberry
jujube
Guava
Grape
Orange
Pomegranate
Apple
Banana
Old Fruit
Hybrid Expert
(With SN =3)
Purple color denotes good samples(Low uncertainty), bad samples are between the range of light blue to orange color. Samples that outside of the islands (i.e., clusters) are between orange and red. (High uncertainty)
Note that only good samples of the training set(old and new fruit) are shown in the background.
both good and bad samples of the test set (old fruit) are shown in the foreground.

## Slide 56
 | Our method | previously proposed Hybrid Expert
Better performance | In our method, the Calibrated Score is 0.99173. | In DeepGD3, the Calibrated Score is 0.98728
Better embedding | The feature distribution is better after using t-SNE for visualization. | The feature distribution is more irregular after using t-SNE for visualization.
Better inference speed | Only one GP model is required during inference stage. (Inference phase took 5.947min +- 2.229min) | Multiple GMM models need to be used, and each piece of data must be input into a different GMM, resulting in slower inference speed. (Inference phase took 25.51 min +- 3.66 min.)
Easier for bayesian optimization | By utilizing calculation and comparing uncertainty methods, only two hyperparameters () need to be optimized for Bayesian optimization. | Each time Bayesian optimization is performed, we need to obtain , and for each corresponding GMM. This allows the GMM to modify the estimated Gaussian distributions for the subsequent classification tasks.
Easier for training | By Gaussian process, we can accurately estimate the uncertainty of the model. This helps us to avoid over-fitting the data, so we do not need to use early stop. | When training with Multi-similarity loss, a large batch size and early stopping are needed to obtain a better feature distribution.
 | Our method | previously proposed Hybrid Expert
Better performance | In our method, the Calibrated Score is 0.99173. | In DeepGD3, the Calibrated Score is 0.98728
Better embedding | The feature distribution is better after using t-SNE for visualization. | The feature distribution is more irregular after using t-SNE for visualization.
Better inference speed | Only one GP model is required during inference stage. (Inference phase took 5.947min +- 2.229min) | Multiple GMM models need to be used, and each piece of data must be input into a different GMM, resulting in slower inference speed. (Inference phase took 25.51 min +- 3.66 min.)
Easier for bayesian optimization |  | 
Easier for training | By Gaussian process, we can accurately estimate the uncertainty of the model. This helps us to avoid over-fitting the data, so we do not need to use early stop. | When training with Multi-similarity loss, a large batch size and early stopping are needed to obtain a better feature distribution.
Part3: Qualitative analysis and Quantitative analysis - Advantages of Our Method Compared to Previously Proposed Hybrid Expert on PCB Dataset

## Slide 57
Ablation study
PART FOUR

## Slide 58
Part4: Ablation study - Comparison of the effect of (a) without stage 2 (b) using GMM and (c) using GP in stage 2
Comparison of the effect of (a) using GMM (b) using GP, in stage 2 and (c) without stage 2 :
Of the experiments above, Stage 1 used Gaussian process classifier for fair comparison.
We will investigate the effects of employing different methods in Stage 2 of our approach to understand the advantage of GP.

## Slide 59
Method | Overkill rate | Leakage rate | Unknown rate | Overkill + Leakage rate | Score
GP is used in Stage 1 (k inducing point) No stage 2. | 1.268% ± 0.446% | 2.481% ± 2.155% | 15.13% ± 3.211% | 3.749% ± 1.709% | 0.94083
GP is used in Stage 1 (k inducing point) GMM is used in Stage 2 | 2.292% ± 1.077% | 1.537% ± 1.361% | 13.7% ± 5.689% | 3.829% ± 1.379% | 0.94468
GP is used in Stage 1 (k inducing point) GP is used in Stage 2 (k*50 inducing point) (Our Method) | 1.187% ± 0.659% | 1.214% ± 0.797% | 12.84% ± 1.915% | 2.4% ± 1.43% | 0.95189
K = number of class
Overkill, Leakage and Unknown rate on other datasets – 8 fruit
Part4: Ablation study - Comparison of the effect of (a) without stage 2 (b) using GMM and (c) using GP in stage 2
The experimental results, averaged over three different dataset splits, utilized all fruit (old + new fruit).
The introduction of the dataset can be found on page 102.
Experiment result show that when GP is used in Stage 2 , it performs better in terms of the Score compared to (a) without stage 2, and (b) using GMM .
Notes: 3.689
3.051
3.877
3.177

## Slide 60
Method | Calibrated Overkill rate | Calibrated Leakage rate | Unknown rate | Calibrated Overkill + Leakage rate | Calibrated Score
GP is used in Stage 1 (k inducing point) No stage 2. | 1.485% ± 0.48% | 2.972% ± 2.594% | 15.13% ± 3.211% | 4.457% ± 2.117% | 0.93852
GP is used in Stage 1 (k inducing point) GMM is used in Stage 2 | 2.628% ± 1.184% | 1.758% ± 1.53% | 13.7% ± 5.689% | 4.385% ± 1.275% | 0.94287
GP is used in Stage 1 (k inducing point) GP is used in Stage 2 (k*50 inducing point) (Our Method) | 1.373% ± 0.796% | 1.406% ± 0.955% | 12.84% ± 1.915% | 2.779% ± 1.723% | 0.95064
K = number of class
Calibrated Overkill, Leakage and Unknown rate on other datasets – 8 fruit
Part4: Ablation study - Comparison of the effect of (a) without stage 2 (b) using GMM and (c) using GP in stage 2
The experimental results, averaged over three different dataset splits, utilized all fruit (old + new fruit).
The introduction of the dataset can be found on page 102.
Experiment result show that when GP is used in Stage 2 , it performs better in terms of the Calibrated Score compared to (a) without stage 2, and (b) using GMM .
Notes: 3.689
3.051
3.877
3.177

## Slide 61
Comparing the impact of spectral normalization :
We compared the effect with and without the utilization of spectral normalization, and further investigated the performance of using spectral normalization under varying parameters.
In experiments conducted exclusively with the data from the new components, we observed that the unknown rate is lower when SN is used, whereas it tends to be higher when SN is not utilized.
Part4: Ablation study - Comparing the impact of spectral normalization

## Slide 62
(a) Hybrid Expert
(With SN =3)
Background : Training set
Foreground : Test set (Red circle and Green Cross )
Part4: Ablation study - t-SNE visualization of Spectral Normalization (SN) using different coefficients – 8 fruit
(b) Hybrid Expert
(With SN =5)
Note that only good samples of the training set(old and new fruit) are shown in the background.
both good and bad samples of the test set (old and new fruit) are shown in the foreground.
We compared the effects of spectral normalization and explored feature distribution with varying parameters. When spectral normalization is applied, bad samples in the test set tend to cluster near the island, while without it, these features are pushed out to sea, potentially increasing the unknown rate.

## Slide 63
Background : Training set
Foreground : Test set (Red circle and Green Cross )
(b) MLP+ GP (Without spectral normalization)
(a) Hybrid Expert
(With SN =7)
Part4: Ablation study - t-SNE visualization of Spectral Normalization (SN) using different coefficients – 8 fruit
We compared the effects of spectral normalization and explored feature distribution with varying parameters. When spectral normalization is applied, bad samples in the test set tend to cluster near the island, while without it, these features are pushed out to sea, potentially increasing the unknown rate.
Note that only good samples of the training set(old and new fruit) are shown in the background.
both good and bad samples of the test set (old and new fruit) are shown in the foreground.

## Slide 64
 | Overkill rate | Leakage rate | Unknown rate | Overkill + Leakage rate | Score
Hybrid Expert (With SN =1) | 2.017% ± 0.625% | 4.313% ± 3.515% | 25.36% ± 1.895% | 6.331% ± 4.138% | 0.9046
Hybrid Expert (With SN =3) | 1.79% ± 1.264% | 4.17% ± 0.984% | 27.61% ± 6.123% | 5.960% ± 1.52% | 0.90006
Hybrid Expert (With SN =5) | 1.603% ± 0.844% | 4.751% ± 3.016% | 21.2% ± 5.067% | 6.354% ± 3.429% | 0.91556
Hybrid Expert (With SN =7) | 2.885% ± 0.347% | 3.263% ± 2.497% | 24.15% ± 4.059% | 6.148% ± 2.234% | 0.90831
Hybrid Expert (Without spectral normalization) | 0.859% ± 0.493% | 1.586% ± 2.481% | 32.28% ± 9.911% | 2.444% ± 2.838% | 0.89995
 | Overkill rate | Leakage rate | Unknown rate | Overkill + Leakage rate | Score
 | 2.017% ± 0.625% | 4.313% ± 3.515% | 25.36% ± 1.895% | 6.331% ± 4.138% | 0.9046
 | 1.79% ± 1.264% | 4.17% ± 0.984% | 27.61% ± 6.123% | 5.960% ± 1.52% | 0.90006
 | 1.603% ± 0.844% | 4.751% ± 3.016% | 21.2% ± 5.067% | 6.354% ± 3.429% | 0.91556
 | 2.885% ± 0.347% | 3.263% ± 2.497% | 24.15% ± 4.059% | 6.148% ± 2.234% | 0.90831
Hybrid Expert (Without spectral normalization) | 0.859% ± 0.493% | 1.586% ± 2.481% | 32.28% ± 9.911% | 2.444% ± 2.838% | 0.89995
Part4: Ablation study - Comparing the impact of spectral normalization
Overkill, Leakage and Unknown rate on other datasets – 8 fruit
The experimental results, averaged over three different dataset splits, utilized new fruit.
The introduction of the dataset can be found on page 102.
From the following content, it can be observed that in the data with only new components, the Unknown rate without spectral normalization is higher compared to the results with spectral normalization.
Notes: 從之前對於不使用spectral normalization的說明以及這張表格的實驗結果可以發現, 不使用spectral normalization會導致我們的演算法無法有效對新類進行預測

## Slide 65
 | Calibrated Overkill rate | Calibrated Leakage rate | Unknown rate | Calibrated Overkill + Leakage rate | Calibrated Score
Hybrid Expert (With SN =1) | 2.717% ± 0.891% | 5.858% ± 4.787% | 25.36% ± 1.895% | 8.575% ± 5.677% | 0.89743
Hybrid Expert (With SN =3) | 2.454% ± 1.74% | 5.858% ± 1.789% | 27.61% ± 6.123% | 8.312% ± 2.524% | 0.89254
Hybrid Expert (With SN =5) | 1.994% ± 0.985% | 6.022% ± 3.68% | 21.2% ± 5.067% | 8.016% ± 4.115% | 0.91026
Hybrid Expert (With SN =7) | 3.804% ± 0.429% | 4.412% ± 3.494% | 24.15% ± 4.059% | 8.215% ± 3.326% | 0.90167
Hybrid Expert (Without spectral normalization) | 1.218% ± 0.622% | 2.267% ± 3.460% | 32.28% ± 9.911% | 3.485% ± 3.942% | 0.89654
 | Calibrated Overkill rate | Calibrated Leakage rate | Unknown rate | Calibrated Overkill + Leakage rate | Calibrated Score
 | 2.717% ± 0.891% | 5.858% ± 4.787% | 25.36% ± 1.895% | 8.575% ± 5.677% | 0.89743
 | 2.454% ± 1.74% | 5.858% ± 1.789% | 27.61% ± 6.123% | 8.312% ± 2.524% | 0.89254
 | 1.994% ± 0.985% | 6.022% ± 3.68% | 21.2% ± 5.067% | 8.016% ± 4.115% | 0.91026
 | 3.804% ± 0.429% | 4.412% ± 3.494% | 24.15% ± 4.059% | 8.215% ± 3.326% | 0.90167
Hybrid Expert (Without spectral normalization) | 1.218% ± 0.622% | 2.267% ± 3.460% | 32.28% ± 9.911% | 3.485% ± 3.942% | 0.89654
Part4: Ablation study - Comparing the impact of spectral normalization
Calibrated Overkill, Leakage and Unknown rate on other datasets – 8 fruit
The experimental results, averaged over three different dataset splits, utilized new fruit.
The introduction of the dataset can be found on page 102.
From the following content, it can be observed that in the data with only new components, the Unknown rate without spectral normalization is higher compared to the results with spectral normalization.
Notes: 從之前對於不使用spectral normalization的說明以及這張表格的實驗結果可以發現, 不使用spectral normalization會導致我們的演算法無法有效對新類進行預測

## Slide 66
 | Overkill rate | Leakage rate | Unknown rate | Overkill + Leakage rate | Score
Hybrid Expert (With SN =1) | 1.446% ± 0.45% | 0% ± 0% | 9.99% ± 1.867% | 1.446% ± 0.45% | 0.96353
Hybrid Expert (With SN =3) | 1.335% ± 0.227% | 0.072% ± 0.062% | 14.34% ± 6.851% | 1.407% ± 0.185% | 0.95081
Hybrid Expert (With SN =5) | 1.05% ± 1.264% | 0% ± 0% | 10.004% ± 3.568% | 1.05% ± 1.264% | 0.96479
Hybrid Expert (With SN =7) | 1.299% ± 0.287% | 0.036% ± 0.063% | 7.47% ± 2.01% | 1.335% ± 0.227% | 0.97158
Hybrid Expert (Without spectral normalization) | 0.542% ± 0.112% | 0% ± 0% | 9.142% ± 3.766% | 0.542% ± 0.112% | 0.96908
 | Overkill rate | Leakage rate | Unknown rate | Overkill + Leakage rate | Score
 | 1.446% ± 0.45% | 0% ± 0% | 9.99% ± 1.867% | 1.446% ± 0.45% | 0.96353
 | 1.335% ± 0.227% | 0.072% ± 0.062% | 14.34% ± 6.851% | 1.407% ± 0.185% | 0.95081
 | 1.05% ± 1.264% | 0% ± 0% | 10.004% ± 3.568% | 1.05% ± 1.264% | 0.96479
 | 1.299% ± 0.287% | 0.036% ± 0.063% | 7.47% ± 2.01% | 1.335% ± 0.227% | 0.97158
Hybrid Expert (Without spectral normalization) | 0.542% ± 0.112% | 0% ± 0% | 9.142% ± 3.766% | 0.542% ± 0.112% | 0.96908
Part4: Ablation study - Comparing the impact of spectral normalization
Overkill, Leakage and Unknown rate on other datasets – 8 fruit
The experimental results, averaged over three different dataset splits, utilized old fruit.
The introduction of the dataset can be found on page 102.
From the following content, it can be observed that in the data with only old components, the Unknown rate without spectral normalization is roughly similar to the results with spectral normalization.
Notes: 從之前對於不使用spectral normalization的說明以及這張表格的實驗結果可以發現, 不使用spectral normalization對於舊的類別則不影響

## Slide 67
 | Calibrated Overkill rate | Calibrated Leakage rate | Unknown rate | Calibrated Overkill + Leakage rate | Calibrated Score
Hybrid Expert (With SN =1) | 1.608% ± 0.509% | 0% ± 0% | 9.99% ± 1.867% | 1.608% ± 0.509% | 0.96299
Hybrid Expert (With SN =3) | 1.557% ± 0.36% | 0.083% ± 0.073% | 14.34% ± 6.851% | 1.66% ± 0.33% | 0.94998
Hybrid Expert (With SN =5) | 1.185% ± 0.842% | 0% ± 0% | 10.004% ± 3.568% | 1.185% ± 0.842% | 0.96434
Hybrid Expert (With SN =7) | 1.409% ± 0.338% | 0.038% ± 0.066% | 7.47% ± 2.01% | 1.447% ± 0.274% | 0.97122
Hybrid Expert (Without spectral normalization) | 0.594% ± 0.103% | 0% ± 0% | 9.142% ± 3.766% | 0.594% ± 0.103% | 0.9689
 | Calibrated Overkill rate | Calibrated Leakage rate | Unknown rate | Calibrated Overkill + Leakage rate | Calibrated Score
 | 1.608% ± 0.509% | 0% ± 0% | 9.99% ± 1.867% | 1.608% ± 0.509% | 0.96299
 | 1.557% ± 0.36% | 0.083% ± 0.073% | 14.34% ± 6.851% | 1.66% ± 0.33% | 0.94998
 | 1.185% ± 0.842% | 0% ± 0% | 10.004% ± 3.568% | 1.185% ± 0.842% | 0.96434
 | 1.409% ± 0.338% | 0.038% ± 0.066% | 7.47% ± 2.01% | 1.447% ± 0.274% | 0.97122
Hybrid Expert (Without spectral normalization) | 0.594% ± 0.103% | 0% ± 0% | 9.142% ± 3.766% | 0.594% ± 0.103% | 0.9689
Calibrated Overkill, Leakage and Unknown rate on other datasets – 8 fruit
Part4: Ablation study - Comparing the impact of spectral normalization
The experimental results, averaged over three different dataset splits, utilized old fruit.
The introduction of the dataset can be found on page 102.
From the following content, it can be observed that in the data with only old components, the Unknown rate without spectral normalization is roughly similar to the results with spectral normalization.

## Slide 68
Method | Overkill rate | Leakage rate | Unknown rate | Overkill + Leakage rate | Score
GP is used in Stage 1 (k inducing point) without stage 2. | 0.059% ± 0.078% | 0.133% ± 0.06% | 2.605% ± 0.885% | 0.191% ± 0.107% | 0.99079
GP is used in Stage 1 (k inducing point) GMM is used in Stage 2 | 0.064% ± 0.011% | 0.081% ± 0.065% | 3.574% ± 1.414% | 0.144% ± 0.055% | 0.98782
GP is used in Stage 1 (k inducing point) GP is used in Stage 2 (k*50 inducing point) (Our Method) | 0.027% ± 0.02% | 0.131% ± 0.059% | 2.237% ± 0.93% | 0.158% ± 0.049% | 0.9921
K = number of class
Overkill, Leakage and Unknown rate on Phison PCB datasets
Part4: Ablation study - Comparison of the effect of (a) without stage 2 (b) using GMM and (c) using GP in stage 2
Experiment result show that when GP is used in Stage 2 , it performs better in terms of the Score compared to (a) without stage 2, and (b) using GMM .
The experimental results, averaged over three different dataset splits, utilized all components (old + new components).
The introduction of the dataset can be found on page 85.

## Slide 69
Method | Calibrated Overkill rate | Calibrated Leakage rate | Unknown rate | Calibrated Overkill + Leakage rate | Calibrated Score
GP is used in Stage 1 (k inducing point) without stage 2. | 0.06% ± 0.08% | 0.136% ± 0.061% | 2.605% ± 0.885% | 0.196% ± 0.11% | 0.99078
GP is used in Stage 1 (k inducing point) GMM is used in Stage 2 | 0.066% ± 0.083% | 0.083% ± 0.066% | 3.574% ± 1.414% | 0.149% ± 0.055% | 0.9878
GP is used in Stage 1 (k inducing point) GP is used in Stage 2 (k*50 inducing point) (Our Method) | 0.027% ± 0.02% | 0.134% ± 0.06% | 2.237% ± 0.93% | 0.161% ± 0.048% | 0.99209
K = number of class
Part4: Ablation study - Comparison of the effect of (a) without stage 2 (b) using GMM and (c) using GP in stage 2
Calibrated Overkill, Leakage and Unknown rate on Phison PCB datasets
The experimental results, averaged over three different dataset splits, utilized all components (old + new components).
The introduction of the dataset can be found on page 85.
Experiment result show that when GP is used in Stage 2 , it performs better in terms of the Calibrated Score compared to (a) without stage 2, and (b) using GMM .

## Slide 70
(a) Hybrid Expert
(With SN =3)
Background : Training set
Foreground : Test set (Red circle and Green Cross )
Part4: Ablation study - t-SNE visualization of Spectral Normalization (SN) using different coefficients -PCB datasets
(b) Hybrid Expert
(With SN =5)
Note that only good samples of the training set(old and new component) are shown in the background.
both good and bad samples of the test set (old and new component) are shown in the foreground.
We compared the effects of using and not using spectral normalization and further investigated the feature distribution when using spectral normalization with varying parameters. In the fruit dataset, we observed more differences when using spectral normalization.

## Slide 71
Background : Training set
Foreground : Test set (Red circle and Green Cross )
(b) Hybrid Expert
(Without spectral normalization)
(a) Hybrid Expert
(With SN =7)
Part4: Ablation study - t-SNE visualization of Spectral Normalization (SN) using different coefficients -PCB datasets
Note that only good samples of the training set(old and new component) are shown in the background.
both good and bad samples of the test set (old and new component) are shown in the foreground.
We compared the effects of using and not using spectral normalization and further investigated the feature distribution when using spectral normalization with varying parameters. In the fruit dataset, we observed more differences when using spectral normalization.

## Slide 72
 | Overkill rate | Leakage rate | Unknown rate | Overkill + Leakage rate | Score
Hybrid Expert (With SN =1) | 0.022% ± 0.008% | 0.34% ± 0.26% | 3.66% ± 2.036% | 0.362% ± 0.254% | 0.98682
Hybrid Expert (With SN =3) | 0.016% ± 0.007% | 0.707% ± 0.589% | 1.005% ± 0.152% | 0.723% ± 0.595% | 0.99426
Hybrid Expert (With SN =5) | 0.037% ± 0.022% | 0.461% ± 0.499% | 1.862% ± 0.744% | 0.498% ± 0.519% | 0.9922
Hybrid Expert (With SN =7) | 0.039% ± 0.053% | 0.497% ± 0.329% | 2.321% ± 1.52% | 0.536% ± 0.38% | 0.99057
Hybrid Expert (Without spectral normalization) | 0.246% ± 0.379% | 0.438% ± 0.359% | 4.803% ± 3.053% | 0.684% ± 0.27% | 0.98209
 | Overkill rate | Leakage rate | Unknown rate | Overkill + Leakage rate | Score
 | 0.022% ± 0.008% | 0.34% ± 0.26% | 3.66% ± 2.036% | 0.362% ± 0.254% | 0.98682
 | 0.016% ± 0.007% | 0.707% ± 0.589% | 1.005% ± 0.152% | 0.723% ± 0.595% | 0.99426
 | 0.037% ± 0.022% | 0.461% ± 0.499% | 1.862% ± 0.744% | 0.498% ± 0.519% | 0.9922
 | 0.039% ± 0.053% | 0.497% ± 0.329% | 2.321% ± 1.52% | 0.536% ± 0.38% | 0.99057
Hybrid Expert (Without spectral normalization) | 0.246% ± 0.379% | 0.438% ± 0.359% | 4.803% ± 3.053% | 0.684% ± 0.27% | 0.98209
Part4: Ablation study - Comparing the impact of spectral normalization
Overkill, Leakage and Unknown rate on Phison PCB datasets
The experimental results, averaged over three different dataset splits, utilized new components.
The introduction of the dataset can be found on page 85.
From the following content, it can be observed that in the data with only new components, the Unknown rate without spectral normalization is higher compared to the results with spectral normalization.
Notes: 從之前對於不使用spectral normalization的說明以及這張表格的實驗結果可以發現, 不使用spectral normalization會導致我們的演算法無法有效對新類進行預測

## Slide 73
 | Calibrated Overkill rate | Calibrated Leakage rate | Unknown rate | Calibrated Overkill + Leakage rate | Calibrated Score
Hybrid Expert (With SN =1) | 0.023% ± 0.008% | 0.353% ± 0.274% | 3.66% ± 2.036% | 0.377% ± 0.267% | 0.98677
Hybrid Expert (With SN =3) | 0.016% ± 0.007% | 0.715% ± 596% | 1.005% ± 0.152% | 0.731% ± 0.602% | 0.99424
Hybrid Expert (With SN =5) | 0.038% ± 0.023% | 0.472% ± 0.514% | 1.862% ± 0.744% | 0.51% ± 0.535% | 0.99216
Hybrid Expert (With SN =7) | 0.041% ± 0.055% | 0.512% ± 0.347% | 2.321% ± 1.52% | 0.553% ± 0.38% | 0.99051
Hybrid Expert (Without spectral normalization) | 0.255% ± 0.392% | 0.468% ± 0.397% | 4.803% ± 3.053% | 0.723% ± 0.298% | 0.98196
 | Calibrated Overkill rate | Calibrated Leakage rate | Unknown rate | Calibrated Overkill + Leakage rate | Calibrated Score
 | 0.023% ± 0.008% | 0.353% ± 0.274% | 3.66% ± 2.036% | 0.377% ± 0.267% | 0.98677
 | 0.016% ± 0.007% | 0.715% ± 596% | 1.005% ± 0.152% | 0.731% ± 0.602% | 0.99424
 | 0.038% ± 0.023% | 0.472% ± 0.514% | 1.862% ± 0.744% | 0.51% ± 0.535% | 0.99216
 | 0.041% ± 0.055% | 0.512% ± 0.347% | 2.321% ± 1.52% | 0.553% ± 0.38% | 0.99051
Hybrid Expert (Without spectral normalization) | 0.255% ± 0.392% | 0.468% ± 0.397% | 4.803% ± 3.053% | 0.723% ± 0.298% | 0.98196
Part4: Ablation study - Comparing the impact of spectral normalization
Calibrated Overkill, Leakage and Unknown rate on Phison PCB datasets
The experimental results, averaged over three different dataset splits, utilized new components.
The introduction of the dataset can be found on page 85.
From the following content, it can be observed that in the data with only new components, the Unknown rate without spectral normalization is higher compared to the results with spectral normalization.
Notes: 從之前對於不使用spectral normalization的說明以及這張表格的實驗結果可以發現, 不使用spectral normalization會導致我們的演算法無法有效對新類進行預測

## Slide 74
 | Overkill rate | Leakage rate | Unknown rate | Overkill + Leakage rate | Score
Hybrid Expert (With SN =1) | 0.03% ± 0.03% | 0.001% ± 0.001% | 1.12% ± 0.958% | 0.03% ± 0.031% | 0.99619
Hybrid Expert (With SN =3) | 0.014% ± 0.007% | 0.002% ± 0.002% | 0.699% ± 0.123% | 0.017% ± 0.009% | 0.9976
Hybrid Expert (With SN =5) | 0.016% ± 0.013% | 0.002% ± 0.003% | 0.673% ± 0.496% | 0.018% ± 0.016% | 0.9977
Hybrid Expert (With SN =7) | 0.021% ± 0.022% | 0.005% ± 0.005% | 0.85% ± 0.775% | 0.026% ± 0.025% | 0.9971
Hybrid Expert (Without spectral normalization) | 0.004% ± 0.005% | 0.004% ± 0.007% | 1.141% ± 1.205% | 0.008% ± 0.012% | 0.99619
 | Overkill rate | Leakage rate | Unknown rate | Overkill + Leakage rate | Score
 | 0.03% ± 0.03% | 0.001% ± 0.001% | 1.12% ± 0.958% | 0.03% ± 0.031% | 0.99619
 | 0.014% ± 0.007% | 0.002% ± 0.002% | 0.699% ± 0.123% | 0.017% ± 0.009% | 0.9976
 | 0.016% ± 0.013% | 0.002% ± 0.003% | 0.673% ± 0.496% | 0.018% ± 0.016% | 0.9977
 | 0.021% ± 0.022% | 0.005% ± 0.005% | 0.85% ± 0.775% | 0.026% ± 0.025% | 0.9971
Hybrid Expert (Without spectral normalization) | 0.004% ± 0.005% | 0.004% ± 0.007% | 1.141% ± 1.205% | 0.008% ± 0.012% | 0.99619
Part4: Ablation study - Comparing the impact of spectral normalization
Overkill, Leakage and Unknown rate on Phison PCB datasets
The experimental results, averaged over three different dataset splits, utilized old components.
The introduction of the dataset can be found on page 85.
From the following content, it can be observed that in the data with only old components, the Unknown rate without spectral normalization is roughly similar to the results with spectral normalization.
Notes: 從之前對於不使用spectral normalization的說明以及這張表格的實驗結果可以發現, 不使用spectral normalization對於舊的類別則不影響

## Slide 75
 | Calibrated Overkill rate | Calibrated Leakage rate | Unknown rate | Calibrated Overkill + Leakage rate | Calibrated Score
Hybrid Expert (With SN =1) | 0.03% ± 0.03% | 0.001% ± 0.001% | 1.12% ± 0.958% | 0.031% ± 0.031% | 0.99619
Hybrid Expert (With SN =3) | 0.015% ± 0.007% | 0.002% ± 0.002% | 0.699% ± 0.123% | 0.017% ± 0.009% | 0.9976
Hybrid Expert (With SN =5) | 0.017% ± 0.014% | 0.002% ± 0.003% | 0.673% ± 0.496% | 0.018% ± 0.016% | 0.9977
Hybrid Expert (With SN =7) | 0.022% ± 0.023% | 0.005% ± 0.005% | 0.85% ± 0.775% | 0.026% ± 0.026% | 0.9971
Hybrid Expert (Without spectral normalization) | 0.004% ± 0.005% | 0.004% ± 0.007% | 1.141% ± 1.205% | 0.009% ± 0.012% | 0.99619
 | Calibrated Overkill rate | Calibrated Leakage rate | Unknown rate | Calibrated Overkill + Leakage rate | Calibrated Score
 | 0.03% ± 0.03% | 0.001% ± 0.001% | 1.12% ± 0.958% | 0.031% ± 0.031% | 0.99619
 | 0.015% ± 0.007% | 0.002% ± 0.002% | 0.699% ± 0.123% | 0.017% ± 0.009% | 0.9976
 | 0.017% ± 0.014% | 0.002% ± 0.003% | 0.673% ± 0.496% | 0.018% ± 0.016% | 0.9977
 | 0.022% ± 0.023% | 0.005% ± 0.005% | 0.85% ± 0.775% | 0.026% ± 0.026% | 0.9971
Hybrid Expert (Without spectral normalization) | 0.004% ± 0.005% | 0.004% ± 0.007% | 1.141% ± 1.205% | 0.009% ± 0.012% | 0.99619
Calibrated Overkill, Leakage and Unknown rate on Phison PCB datasets
Part4: Ablation study - Comparing the impact of spectral normalization
The experimental results, averaged over three different dataset splits, utilized old components.
The introduction of the dataset can be found on page 85.
From the following content, it can be observed that in the data with only old components, the Unknown rate without spectral normalization is roughly similar to the results with spectral normalization.
Notes: 從之前對於不使用spectral normalization的說明以及這張表格的實驗結果可以發現, 不使用spectral normalization對於舊的類別則不影響

## Slide 76
Summary
PART FIVE

## Slide 77
Part5: Summary - Conclusion
We propose a Hybrid Expert which is a combination of MLP classifier (Defect detector branch) and Gaussian Process classifier (Component Classifier branch).
By varying the search space of Bayesian optimization, our proposed method can achieve different results according to different purposes.
Our method achieved an improved Calibrated Score of 0.99209 compared to previously proposed Hybrid Expert’s 0.98728 for Phison dataset. For 8-fruit dataset, from 0.9317 to 0.95064.
Future works :
  By optimizing the architecture of the feature extractor, the features are closer to the Gaussian distribution, the overall performance can be improved.
  To predict bad samples of new component, the diffusion model can be used to edit images or generate new defect images and use these data for training to address the poor detection performance for new defects.

## Slide 78
Thanks for Your Attention
Reporter：陳昱廷
Date：2023/09/25

## Slide 79
Appendix

## Slide 80
Appendix - Dataset: Introduction
 | Phison Dataset
Number of images | 1,364,400
Component types | 35 different components
Defect types | good, missing, shift, stand, broken, short
Label information | Each image is labeled with 1 type of component and 1 type of defect.
Good
Missing
Shift
Stand
Broken
Short
Missing and standing samples are difficult to be visually recognized as specific components.
We treat them as two separate components.
Figure 2.1. Visualization of each defect types
Summary for Phison Dataset

## Slide 81
Appendix - Dataset: Introduction
Since the appearance of some components is very similar, we decided to group similar components into the same category.
Visualization of each component

## Slide 82
Appendix - Dataset: dataset grouping
Feature Extractor
Feature Extractor : MobileNetV3Large (pretrained)
Clustering Method : AgglomerativeClustering , Kmeans
Clustering
Data Selector
( , )
The data selector picks out good samples from the entire dataset and downsamples them. After downsampling, each component contains up to 10,000 good samples.
Use silhouette analysis to determine the number of groups.
Grouping Procedure Stage 1 : Clustering .

## Slide 83
Calculate the sample sizes of each component in each group based on the clustering results )
2. = Sample sizes of component in group g , = Sample sizes of component in
3. : assign component to group g
Appendix - Algorithm for Data grouping
Data Regrouping
,
Grouping Procedure Stage 2 : Data grouping.

## Slide 84
Samples of all component (13 components)
Samples of old components (7 components)
Samples of new components (6 components)
Samples of 3 new components
Samples of 3 new components
Good Samples
Bad Samples
Good Samples
Bad Samples
50% good samples of each new components
Defect Training set
Component Training set
Good, missing, stand samples in defect training set are used for component training set.
10% of the old component samples are used for the test set.
Test set
Validation set
10% of the old component samples are used for the validation set.
Note that the training set, validation set, and test set are disjoint sets.
Good samples of new components are available for model training.
Appendix - Dataset: Train/Val/Test Split

## Slide 85
Appendix - Number of old and new component samples in the test set of each split.
Test set |  | 
 | Old component | new component
Split A | 71985 | 21911
Split B | 91006 | 198749
Split C | 110339 | 118744
Below is a table that introduces the number of old and new component samples in the test set of each split.

## Slide 86
Appendix - Algorithm: MobileNetV3 Large
The ImageNet pre-trained MobileNetV3 Large [3] was used as the feature extractor . We use it because of its fast inference speed.
MobileNetV3 Large model architecture. Modified from [3]. SE denotes whether there is a Squeeze-and-Excitation [4] in that block. NL denotes the type of nonlinearity used. HS denotes h-swish and RE denotes ReLU. NBN denotes no batch normalization. s denotes stride.
[3] Howard, A., Sandler, M., Chu, G., Chen, L. C., Chen, B., Tan, M., ... & Adam, H. (2019). Searching for mobilenetv3. In Proceedings of the IEEE/CVF international conference on computer vision (pp. 1314-1324).
[4] Hu, J., Shen, L., & Sun, G. (2018). Squeeze-and-excitation networks. In Proceedings of the IEEE conference on computer vision and pattern recognition (pp. 7132-7141).

## Slide 87
Appendix
- Element in each ablative architecture
Feature extractor | Shared Encoder | Component Projection Network
 |  | 
Cross Entropy Loss
Variational
ELBO
Component Projection Network
{ Good , Bad/Missing , Bad/Stand, Bad/Short, Bad/Broke, Bad/Shift }
{Good , Bad/Missing , Bad/Stand}
Inducing points = number of component types
Feature Extractor
Shared Encoder
Feature Extractor
Shared Encoder
Shared weight

## Slide 88
Feature extractor | Shared Encoder | Component Projection Network
 |  | 
Cross Entropy Loss
Variational
ELBO
Inducing points = number of component types
Appendix
- Element in each ablative architecture
{ Good , Bad/Missing , Bad/Stand, Bad/Short, Bad/Broke, Bad/Shift }
{Good , Bad/Missing , Bad/Stand}
Feature Extractor
Shared Encoder
Feature Extractor
Shared Encoder
Shared weight

## Slide 89
Feature extractor | Shared Encoder | Component Projection Network
 |  | 
Cross Entropy Loss
Variational
ELBO
Component Projection Network
Inducing points = number of component types
Appendix
- Element in each ablative architecture
{ Good , Bad/Missing , Bad/Stand, Bad/Short, Bad/Broke, Bad/Shift }
{Good , Bad/Missing , Bad/Stand}
Feature Extractor
Feature Extractor
Shared weight

## Slide 90
Feature extractor | Shared Encoder | Component Projection Network
 |  | 
Cross Entropy Loss
Variational
ELBO
Inducing points = number of component types
Appendix
- Element in each ablative architecture
{ Good , Bad/Missing , Bad/Stand, Bad/Short, Bad/Broke, Bad/Shift }
{Good , Bad/Missing , Bad/Stand}
Feature Extractor
Feature Extractor
Shared weight

## Slide 91
Appendix - Effect of each element in our method (overkill and leakage rate)
Feature extractor | Shared Encoder | Component Projection Network | Overkill rate | Leakage rate | Overkill + Leakage rate | Unknown rate
 |  |  | 0.06% ± 0.089% | 0.34% ± 0.228% | 0.4% ± 0.178% | 24.55% ± 28.21%
 |  |  | 0.01% ± 0.011% | 0.527% ± 0.334% | 0.538% ± 0.344% | 1.797% ± 0.986%
 |  |  | 0.032% ± 0.023% | 0.17% ± 0.106% | 0.202% ± 0.11% | 2.177% ± 0.613%
 |  |  | 0.059% ± 0.078% | 0.133% ± 0.06% | 0.191% ± 0.107% | 2.605% ± 0.885%
Experimental results obtained by incorporating various elements in the model architecture allow us to select the most suitable model structure based on these outcomes.
The experimental results, averaged over three different dataset splits, utilized all components (old + new components).
The introduction of the dataset can be found on page 83.

## Slide 92
Appendix - Effect of each element in our method (calibrated overkill and calibrated leakage rate)
Feature extractor | Shared Encoder | Component Projection Network | Calibrated Overkill rate | Calibrated Leakage rate | Calibrated Overkill + Leakage rate | Unknown rate
 |  |  | 0.063% ± 0.091% | 0.501% ± 0.31% | 0.564% ± 0.221% | 24.55% ± 28.21%
 |  |  | 0.011% ± 0.011% | 0.539% ± 0.346% | 0.55% ± 0.356% | 1.797% ± 0.986%
 |  |  | 0.033% ± 0.024% | 0.173% ± 0.107% | 0.206% ± 0.111% | 2.177% ± 0.613%
 |  |  | 0.06% ± 0.08% | 0.136% ± 0.061% | 0.196% ± 0.11% | 2.605% ± 0.885%
Experimental results obtained by incorporating various elements in the model architecture allow us to select the most suitable model structure based on these outcomes.
The experimental results, averaged over three different dataset splits, utilized all components (old + new components).
The introduction of the dataset can be found on page 83.

## Slide 93
Number of defect types | Overkill rate | Leakage rate | Calibrated Overkill rate | Calibrated Leakage rate | Unknown rate
Two types of defects | 0.027% ± 0.02% | 0.131% ± 0.059% | 0.027% ± 0.02% | 0.134% ± 0.06% | 2.237% ± 0.93%
Six types of defects | 0.042% ± 0.04% | 0.215% ± 0.114% | 0.044% ± 0.041% | 0.224% ± 0.119% | 3.684% ± 0.362%
Appendix - Performance comparison: 2 types of defects vs. 6 types of defects
The experimental results, averaged over three different dataset splits, utilized all components (old + new components).
The introduction of the dataset can be found on page 83.
We will conduct experiments using two different quantities of defect types. The "2 types of defects" refer to classifying defect types as "good" and "bad." The "6 types of defects" pertain to the original component defect types, including good, missing, stand, short, broken, and shift. Through this experiment, we will determine which method is more effective to use in the upper branch.

## Slide 94
Appendix - Comparing the performance of different metric learning methods with previously proposed Hybrid Expert
Method | Overkill rate | Leakage rate | Unknown rate | Overkill + Leakage rate | Score
Triplet | 0.261% ± 0.14% | 0.726% ± 1.063% | 8.431% ± 4.177% | 0.987% ± 0.924% | 0.9698
CosFace | 0.229% ± 0.105% | 0.132% ± 0.088% | 6.886% ± 1.276% | 0.361% ± 0.015% | 0.9766
ArcFace | 0.12% ± 0.025% | 0.315% ± 0.098% | 5.343% ± 3.288% | 0.436% ± 0.121% | 0.9812
Multi-similarity | 0.108% ± 0.033% | 0.063% ± 0.075% | 3.706% ± 2.270% | 0.171% ± 0.108% | 0.9873
Our Method | 0.027% ± 0.02% | 0.131% ± 0.059% | 2.237% ± 0.93% | 0.158% ± 0.049% | 0.9921
Overkill, Leakage and Unknown rate on Phison PCB datasets
The experimental results, averaged over three different dataset splits, utilized all components (old + new components).
The introduction of the dataset can be found on page 83.
We compared the performance of different metric learning methods used in the lower branch of the previously proposed Hybrid Expert.

## Slide 95
Method | Calibrated Overkill rate | Calibrated Leakage rate | Unknown rate | Calibrated Overkill + Leakage rate | Calibrated Score
Triplet | 0.282% ± 0.145% | 0.818% ± 1.208% | 8.431% ± 4.177% | 1.1% ± 1.062% | 0.9694
CosFace | 0.245% ± 0.111% | 0.142% ± 0.097% | 6.886% ± 1.276% | 0.387% ± 0.019% | 0.9765
ArcFace | 0.126% ± 0.023% | 0.331% ± 0.094% | 5.343% ± 3.288% | 0.458% ± 0.113% | 0.9765
Multi-similarity | 0.112% ± 0.035% | 0.065% ± 0.078% | 3.706% ± 2.270% | 0.178% ± 0.113% | 0.98728
Our Method | 0.027% ± 0.02% | 0.134% ± 0.06% | 2.237% ± 0.93% | 0.161% ± 0.048% | 0.99209
Calibrated Overkill, Leakage and Unknown rate on Phison PCB datasets
Appendix - Comparing the performance of different metric learning methods with previously proposed Hybrid Expert
The experimental results, averaged over three different dataset splits, utilized all components (old + new components).
The introduction of the dataset can be found on page 83.
We compared the performance of different metric learning methods used in the lower branch of the previously proposed Hybrid Expert.

## Slide 96
How to determine the threshold for unknown prediction?
Calculate the predicted probability of samples from training set and validation set with trained model.
Estimate the uncertainty of the samples from training set and validation set using the predicted probability, O : Number of class output
Find the mean () and standard deviation of all the uncertainty value from each component.
Set the threshold (T) with the following formula: T =
Find the that produces the best performance by observing the variation of the overkill rate, leakage rate, and unknown rate in the training and validation sets.
(, optimized by Bayesian optimizer , Find the best average of Overkill rate, Leakage rate, )
Appendix - Algorithm for Unknown Prediction – Method 1
{1, 2, 3, } is the name of training component
Notes: 計算所有training set 的 sample的預測機率，並以這些預測機率計算所有training set 的 sample 的uncertainty

## Slide 97
Component Classifier branch :
  If ( U >):
  = Unknown
  If ( ):
  = Bad
  If ( ):
  = Good
0
good
bad
unknown
Normalized Uncertainty
1
Find the , that produces the best performance by observing the variation of the overkill rate, leakage rate, and unknown rate in the training and validation sets.
, optimized by Bayesian optimizer , Find the best average of Overkill rate, Leakage rate,
Appendix - Algorithm for Unknown Prediction – Method 2
K : number of component types
{1, 2, 3, ,K} is the name of training component

## Slide 98
 | Overkill rate | Leakage rate | Unknown rate | Overkill + Leakage rate | Score
Uncertainty ( Method 1 ) | 0.055% ± 0.046% | 0.116% ± 0.046% | 2.335% ± 0.717% | 0.171% ± 0.028% | 0.99174
Normalized uncertainty ( Method 1 ) | 0.257% ± 0.378% | 0.108% ± 0.058% | 2.335% ± 0.643% | 0.365% ± 0.32% | 0.99109
Normalized uncertainty ( Method 2 ) | 0.027% ± 0.02% | 0.131% ± 0.059% | 2.237% ± 0.93% | 0.158% ± 0.049% | 0.9921
Appendix - Comparison between Uncertainty and Normalized uncertainty
Overkill, Leakage and Unknown rate on Phison PCB datasets
The experimental results, averaged over three different dataset splits, utilized all components (old + new components).
The introduction of the dataset can be found on page 83.
We compared the performance of different methods used in the different uncertainty estimate methods of the Hybrid Expert.

## Slide 99
 | Calibrated Overkill rate | Calibrated Leakage rate | Unknown rate | Calibrated Overkill + Leakage rate | Calibrated Score
Uncertainty ( Method 1 ) | 0.056% ± 0.048% | 0.119% ± 0.047% | 2.335% ± 0.717% | 0.175% ± 0.027% | 0.99173
Normalized uncertainty ( Method 1 ) | 0.264% ± 0.389% | 0.111% ± 0.059% | 2.335% ± 0.643% | 0.374% ± 0.33% | 0.99106
Normalized uncertainty ( Method 2 ) | 0.027% ± 0.02% | 0.134% ± 0.06% | 2.237% ± 0.93% | 0.161% ± 0.048% | 0.99209
Appendix - Comparison between Uncertainty and Normalized uncertainty
Calibrated Overkill, Leakage and Unknown rate on Phison PCB datasets
We compared the performance of different methods used in the different uncertainty estimate methods of the Hybrid Expert.
The experimental results, averaged over three different dataset splits, utilized all components (old + new components).
The introduction of the dataset can be found on page 83.

## Slide 100
(b) CosFace Loss
(a) Triplet Loss
Note that only good samples of the training set are shown in the background.
Background : Training set
Foreground : Test set (Red circle and Green Cross )
Appendix - t-SNE visualization of on other loss function -PCB datasets
stand
missing

## Slide 101
(b) multi-similarity Loss
(a) ArcFace Loss
Note that only good samples of the training set are shown in the background.
Background : Training set
Foreground : Test set (Red circle and Green Cross )
Appendix - t-SNE visualization of on other loss function -PCB datasets
stand
missing

## Slide 102
Train / val set :
Upper branch of hybrid expert uses 8 fruits. 6 of them has both good and bad(old fruit) . 2 of them only has good samples (new fruit).
Lower branch of hybrid expert uses 8 fruits. ALL of them only has good samples.
Testset :
Use 8 fruit , ALL of them has good and bad samples.
Number of Good sample images : 600 in each class
Number of Bad sample images : 600 in each class
https://data.mendeley.com/datasets/bdd69gyhv8/1
Appendix - The introduction of the dataset – 8 fruit
With different random seeds, two different fruit will be selected as the new object.
The new object is then not using bad samples in the Defect Detector branch.

## Slide 103
(b) Stage 2
Note that only good samples of the training set are shown in the background.
Background : Training set
Foreground : Inducing point (Red circle)
(a) Stage 1
Appendix - t-SNE visualization for inducing point - 8 fruit

## Slide 104
(b)
(a)
Note that only good samples of the training set are shown in the background.
Background : Training set
Foreground : Test set (Red circle and Green Cross )
Appendix - t-SNE visualization for previously proposed Hybrid Expert - 8 fruit

## Slide 105
(c) ArcFace Loss
(b) CosFace Loss
(a) Triplet Loss
Note that only good samples of the training set are shown in the background.
Background : Training set
Foreground : Test set (Red circle and Green Cross )
Appendix - t-SNE visualization of on other loss function - 8 fruit

## Slide 106
Method | Overkill rate | Leakage rate | Unknown rate | Overkill + Leakage rate | Score
Triplet | 5.717% ± 7.604% | 1.214% ± 1.896% | 16.67% ± 10.49% | 6.931% ± 6.845% | 0.92628
CosFace | 5.663% ± 2.747% | 0.971% ± 1.133% | 12.86% ± 8.053% | 6.634% ± 3.628% | 0.93818
ArcFace | 4.612% ± 1.699% | 1.106% ± 1.514% | 13.92% ± 6.594% | 5.717% ± 2.995% | 0.93801
Multi-similarity | 2.967% ± 0.124% | 0% ± 0% | 18.47% ± 10.69% | 2.967% ± 0.124% | 0.93403
Our Method | 1.187% ± 0.659% | 1.214% ± 0.797% | 12.84% ± 1.915% | 2.4% ± 1.43% | 0.95189
Overkill, Leakage and Unknown rate on other datasets – 8 fruit
Appendix - Comparing the performance of different metric learning methods with previously proposed Hybrid Expert
We compared the performance of different methods used in the lower branch of the previously proposed Hybrid Expert.
The experimental results, averaged over three different dataset splits, utilized all fruit (old + new fruit).
The introduction of the dataset can be found on page 100.

## Slide 107
Method | Calibrated Overkill rate | Calibrated Leakage rate | Unknown rate | Calibrated Overkill + Leakage rate | Calibrated Score
Triplet | 7.772% ± 10.88% | 1.372% ± 2.147% | 16.67% ± 10.49% | 9.144% ± 9.947% | 0.91936
CosFace | 6.692% ± 3.517% | 1.13% ± 1.298% | 12.86% ± 8.053% | 7.822% ± 4.447% | 0.93442
ArcFace | 5.472% ± 2.287% | 1.34% ± 1.832% | 13.92% ± 6.594% | 6.812% ± 3.824% | 0.9345
Multi-similarity | 3.689% ± 0.585% | 0% ± 0% | 18.47% ± 10.69% | 3.689% ± 0.585% | 0.9317
Our Method | 1.373% ± 0.796% | 1.406% ± 0.955% | 12.84% ± 1.915% | 2.779% ± 1.723% | 0.95064
Calibrated Overkill, Leakage and Unknown rate on other datasets – 8 fruit
Appendix - Comparing the performance of different metric learning methods with previously proposed Hybrid Expert
We compared the performance of different methods used in the lower branch of the previously proposed Hybrid Expert.
The experimental results, averaged over three different dataset splits, utilized all fruit (old + new fruit).
The introduction of the dataset can be found on page 100.

## Slide 108
 | Overkill rate | Leakage rate | Unknown rate | Overkill + Leakage rate | Score
Uncertainty ( Method 1 ) | 1.186% ± 0.734% | 1.348% ± 1.335% | 13.4% ± 2.621% | 2.535% ± 1.425% | 0.94979
Normalized uncertainty ( Method 1 ) | 1.214% ± 0.719% | 1.456% ± 1.351% | 13.4% ± 2.581% | 2.67% ± 1.485% | 0.94935
Normalized uncertainty ( Method 2 ) | 1.187% ± 0.659% | 1.214% ± 0.797% | 12.84% ± 1.915% | 2.4% ± 1.43% | 0.95189
Appendix - Comparison between Uncertainty and Normalized uncertainty
Overkill, Leakage and Unknown rate on other datasets – 8 fruit
The experimental results, averaged over three different dataset splits, utilized all fruit (old + new fruit).
The introduction of the dataset can be found on page 100.
We compared the performance of different methods used in the different uncertainty estimate methods of the Hybrid Expert.

## Slide 109
 | Calibrated Overkill rate | Calibrated Leakage rate | Unknown rate | Calibrated Overkill + Leakage rate | Calibrated Score
Uncertainty ( Method 1 ) | 1.361% ± 0.822% | 1.586% ± 1.597% | 13.4% ± 2.621% | 2.947% ± 1.68% | 0.94845
Normalized uncertainty ( Method 1 ) | 1.395% ± 0.815% | 1.712% ± 1.607% | 13.4% ± 2.581% | 3.106% ± 1.749% | 0.94791
Normalized uncertainty ( Method 2 ) | 1.373% ± 0.796% | 1.406% ± 0.955% | 12.84% ± 1.915% | 2.779% ± 1.723% | 0.95064
Appendix - Comparison between Uncertainty and Normalized uncertainty
Calibrated Overkill, Leakage and Unknown rate on other datasets – 8 fruit
The experimental results, averaged over three different dataset splits, utilized all fruit (old + new fruit).
The introduction of the dataset can be found on page 100.
We compared the performance of different methods used in the different uncertainty estimate methods of the Hybrid Expert.

## Slide 110
 | Expert 2 Unknown rate | Hybrid Expert Unknown rate
MLP+ GP (With SN =1) | 1.321% ± 1.193% | 13.4% ± 2.621%
MLP+ GP (With SN =3) | 0.998% ± 1.116% | 12.84% ± 1.915%
MLP+ GP (With SN =5) | 0.512% ± 0.888% | 17.69% ± 4.659%
MLP+ GP (With SN =7) | 0.216% ± 0.374% | 11.7% ± 1.792%
MLP+ GP (Without spectral normalization) | 5.016% ± 2.121% | 15.05% ± 2.176%
 | Expert 2 Unknown rate | Hybrid Expert Unknown rate
 | 1.321% ± 1.193% | 13.4% ± 2.621%
 | 0.998% ± 1.116% | 12.84% ± 1.915%
 | 0.512% ± 0.888% | 17.69% ± 4.659%
 | 0.216% ± 0.374% | 11.7% ± 1.792%
MLP+ GP (Without spectral normalization) | 5.016% ± 2.121% | 15.05% ± 2.176%
Appendix - Effectiveness of Spectral Normalization (SN) using different coefficients – 8 fruit
The experimental results, averaged over three different dataset splits, utilized all fruit (old + new fruit).
The introduction of the dataset can be found on page 100.
To assess the effectiveness of Spectral Normalization (SN) , we evaluate it by observing the 'unknown' classification by Expert 2.

## Slide 111
Appendix - The introduction of the dataset - 3 fruits
With different random seeds, a different fruit will be selected as the new object.
The new object is then not using bad samples in the Defect Detector branch.
Train / val set :
Upper branch of hybrid expert uses 3 fruits. 2 of them has both good and bad(old fruit). 1 of them only has good samples(new fruit).
Lower branch of hybrid expert uses 3 fruits. ALL of them only has good samples.
Testset :
Use 8 fruit , ALL of them has good and bad samples.

## Slide 112
good
bad
Appendix
- t-sne visualization of z from train and test samples
Background : Training set
Foreground : Test set (Red circle and Green Cross )
Upper branch
(Defect detection)
Gaussian Process classifier
ties to
prediction
Uncertainty
Converter
prediction
Uncertainty
to defect
converter
Feature Extractor
Prediction
Combiner
MLP classifier
Expert 1 : use only the upper branch
Notes: In (a) Expert 1, the bad test samples overlap with the good test samples. In addition, missing and stand islands are mixed in the feature space
In (b) Expert 2, missing and stand islands are not mixed in the feature space.
The missing and stand islands are separated in (c) Hybrid Expert.
Furthermore, the bad test samples are push away from the good test samples as illustrated in (c) Hybrid Expert.

## Slide 113
Apple
Banana
Orange
Background : Training set
Foreground : Test set (Red circle and Green Cross )
(b) Lower branch
(Component classification)
Gaussian Process classifier
ties to
prediction
Uncertainty
Converter
prediction
Uncertainty
to defect
converter
Feature Extractor
Prediction
Combiner
MLP classifier
Expert 2 : use only the lower branch
Appendix
- t-sne visualization of z from train and test samples
Notes: In (a) Expert 1, the bad test samples overlap with the good test samples. In addition, missing and stand islands are mixed in the feature space
In (b) Expert 2, missing and stand islands are not mixed in the feature space.
The missing and stand islands are separated in (c) Hybrid Expert.
Furthermore, the bad test samples are push away from the good test samples as illustrated in (c) Hybrid Expert.

## Slide 114
Background : Training set
Foreground : Test set (Red circle and Green Cross )
Gaussian Process classifier
ties to
prediction
Uncertainty
Converter
prediction
Uncertainty
to defect
converter
Feature Extractor
Prediction
Combiner
MLP classifier
(c) Hybrid Expert
Hybrid Expert : Base on DUE
Appendix
- t-sne visualization of z from train and test samples
Notes: In (a) Expert 1, the bad test samples overlap with the good test samples. In addition, missing and stand islands are mixed in the feature space
In (b) Expert 2, missing and stand islands are not mixed in the feature space.
The missing and stand islands are separated in (c) Hybrid Expert.
Furthermore, the bad test samples are push away from the good test samples as illustrated in (c) Hybrid Expert.

## Slide 115
(b) Stage 2
Note that only good samples of the training set are shown in the background.
Background : Training set
Foreground : Inducing point (Red circle)
(a) Stage 1
Appendix - t-SNE visualization for inducing point - 3 fruit

## Slide 116
(b)
(a)
Note that only good samples of the training set are shown in the background.
Background : Training set
Foreground : Test set (Red circle and Green Cross )
Appendix - t-SNE visualization for previously proposed Hybrid Expert - 3 fruit

## Slide 117
(c) ArcFace Loss
(b) CosFace Loss
(a) Triplet Loss
Note that only good samples of the training set are shown in the background.
Background : Training set
Foreground : Test set (Red circle and Green Cross )
Appendix - t-SNE visualization of on other loss function - 3 fruit

## Slide 118
 | Overkill rate | Leakage rate | Unknown rate | Overkill + Leakage rate | Score
Uncertainty ( Method 1 ) | 0.408% ± 0.074% | 0.964% ± 1.297% | 20.08% ± 6.323% | 1.371% ± 1.31% | 0.93482
Normalized uncertainty ( Method 1 ) | 0.383% ± 0.057% | 1.087% ± 1.234% | 20.35% ± 6.714% | 1.47% ± 1.242% | 0.93375
Normalized uncertainty ( Method 2 ) | 0.544% ± 0.043% | 1.964% ± 1.553% | 9.007% ± 2.468% | 2.508% ± 1.563% | 0.96299
Appendix - Comparison between Uncertainty and Normalized uncertainty
The experimental results, averaged over three different dataset splits, utilized all fruit (old + new fruit).
The introduction of the dataset can be found on page 109.
We compared the performance of different methods used in the different uncertainty estimate methods of the Hybrid Expert.
Overkill, Leakage and Unknown rate on other datasets – 3 fruit

## Slide 119
 | Calibrated Overkill rate | Calibrated Leakage rate | Unknown rate | Calibrated Overkill + Leakage rate | Calibrated Score
Uncertainty ( Method 1 ) | 0.517% ± 0.133% | 1.169% ± 1.521% | 20.08% ± 6.323% | 1.685% ± 1.521% | 0.93378
Normalized uncertainty ( Method 1 ) | 0.487% ± 0.115% | 1.344% ± 1.448% | 20.35% ± 6.714% | 1.831% ± 1.453% | 0.93256
Normalized uncertainty ( Method 2 ) | 0.599% ± 0.064% | 2.162% ± 1.69% | 9.007% ± 2.468% | 2.761% ± 1.705% | 0.96299
Appendix - Comparison between Uncertainty and Normalized uncertainty
The experimental results, averaged over three different dataset splits, utilized all fruit (old + new fruit).
The introduction of the dataset can be found on page 109.
We compared the performance of different methods used in the different uncertainty estimate methods of the Hybrid Expert.
Overkill, Leakage and Unknown rate on other datasets – 3 fruit

## Slide 120
Method | Overkill rate | Leakage rate | Unknown rate | Overkill + Leakage rate | Score
GP is used in Stage 1 (k inducing point) No stage 2. | 0.445% ± 0.17% | 1.866% ± 1.52% | 17.31% ± 4.751% | 2.31% ± 1.478% | 0.93938
GP is used in Stage 1 (k inducing point) GMM is used in Stage 2 | 1.013% ± 0.396% | 0.729% ± 1.017% | 19.4% ± 9.296% | 1.742% ± 1.408% | 0.93545
GP is used in Stage 1 (k inducing point) GP is used in Stage 2 (k*50 inducing point) (Our Method) | 0.544% ± 0.043% | 1.964% ± 1.553% | 9.007% ± 2.468% | 2.508% ± 1.563% | 0.96299
K = number of class
Appendix - Comparison of the effect of (a) using GMM (b) using GP, in stage 2 and (c) without stage 2
Overkill, Leakage and Unknown rate on other datasets – 3 fruit
Of the experiments above, Stage 1 used Gaussian process classifier for fair comparison.
We will investigate the effects of employing different methods in Stage 2 of our approach.
The experimental results, averaged over three different dataset splits, utilized all fruit (old + new fruit).
The introduction of the dataset can be found on page 109.

## Slide 121
Method | Calibrated Overkill rate | Calibrated Leakage rate | Unknown rate | Calibrated Overkill + Leakage rate | Calibrated Score
GP is used in Stage 1 (k inducing point) No stage 2. | 0.538% ± 0.209% | 2.201% ± 1.703% | 17.31% ± 4.751% | 2.739% ± 1.609% | 0.93798
GP is used in Stage 1 (k inducing point) GMM is used in Stage 2 | 1.307% ± 0.663% | 1.01% ± 1.446% | 19.4% ± 9.296% | 2.317% ± 2.102% | 0.93355
GP is used in Stage 1 (k inducing point) GP is used in Stage 2 (k*50 inducing point) (Our Method) | 0.599% ± 0.064% | 2.162% ± 1.69% | 9.007% ± 2.468% | 2.761% ± 1.705% | 0.96217
K = number of class
Calibrated Overkill, Leakage and Unknown rate on other datasets – 3 fruit
Appendix - Comparison of the effect of (a) using GMM (b) using GP, in stage 2 and (c) without stage 2
Of the experiments above, Stage 1 used Gaussian process classifier for fair comparison.
We will investigate the effects of employing different methods in Stage 2 of our approach.
The experimental results, averaged over three different dataset splits, utilized all fruit (old + new fruit).
The introduction of the dataset can be found on page 109.

## Slide 122
Method | Overkill rate | Leakage rate | Unknown rate | Overkill + Leakage rate | Score
Triplet | 1.273% ± 1.082% | 0.358% ± 0.525% | 25.43% ± 6.591% | 1.631% ± 0.929% | 0.91976
CosFace | 0% ± 0% | 6.61% ± 3.099% | 55.12% ± 3.713% | 6.61% ± 3.099% | 0.83744
ArcFace | 1.421% ± 2.461% | 3.261% ± 3.961% | 53.22% ± 7.877% | 4.683% ± 3.095% | 0.84703
Multi-similarity | 0.828% ± 0.356% | 0.247% ± 0.428% | 28.24% ± 4.392% | 1.075% ± 0.162% | 0.9144
Our Method | 0.544% ± 0.043% | 1.964% ± 1.553% | 9.007% ± 2.468% | 2.508% ± 1.563% | 0.96299
Overkill, Leakage and Unknown rate on other datasets – 3 fruit
Appendix - Comparing the performance of different metric learning methods with previously proposed Hybrid Expert
We compared the performance of different metric learning methods used in the lower branch of the previously proposed Hybrid Expert.
The experimental results, averaged over three different dataset splits, utilized all fruit (old + new fruit).
The introduction of the dataset can be found on page 109.

## Slide 123
Method | Calibrated Overkill rate | Calibrated Leakage rate | Unknown rate | Calibrated Overkill + Leakage rate | Calibrated Score
Triplet | 1.729% ± 1.486% | 0.445% ± 0.637% | 25.43% ± 6.591% | 2.174% ± 1.251% | 0.91797
CosFace | 0% ± 0% | 14.4% ± 5.867% | 55.12% ± 3.713% | 14.4% ± 5.867% | 0.81405
ArcFace | 2.602% ± 4.507% | 7.15% ± 8.355% | 53.22% ± 7.877% | 9.753% ± 6.335% | 0.83086
Multi-similarity | 1.174% ± 0.564% | 0.331% ± 0.573% | 28.24% ± 4.392% | 1.505% ± 0.268% | 0.91299
Our Method | 0.599% ± 0.064% | 2.162% ± 1.69% | 9.007% ± 2.468% | 2.761% ± 1.705% | 0.96217
Calibrated Overkill, Leakage and Unknown rate on other datasets – 3 fruit
Appendix - Comparing the performance of different metric learning methods with previously proposed Hybrid Expert
The experimental results, averaged over three different dataset splits, utilized all fruit (old + new fruit).
The introduction of the dataset can be found on page 109.
We compared the performance of different metric learning methods used in the lower branch of the previously proposed Hybrid Expert.

## Slide 124
Method | Overkill rate | Leakage rate | Unknown rate | Overkill + Leakage rate
Expert 1 | 0.321% ± 0.273% | 6.301% ± 4.911% | - | 6.622% ± 4.644%
Expert 2 | 2.669% ± 2.089% | 26.946% ± 3.885% | 5.992% ± 2.719% | 29.62% ± 3.225%
Hybrid Expert | 0.544% ± 0.043% | 1.964% ± 1.553% | 9.007% ± 2.468% | 2.508% ± 1.563%
Overkill, Leakage and Unknown rate on other datasets – 3 fruit
Appendix - Comparing the Performance between Expert 1, Expert 2, and Hybrid Expert
We separately evaluate the performance of Expert 1 and Expert 2, comparing them to our hybrid expert approach to understand the limitations of using only one of them.
The experimental results, averaged over three different dataset splits, utilized all fruit (old + new fruit).
The introduction of the dataset can be found on page 109.

## Slide 125
Method | Calibrated Overkill rate | Calibrated Leakage rate | Unknown rate | Calibrated Overkill + Leakage Rate
Expert 1 | 0.321% ± 0.273% | 6.301% ± 4.911% | - | 6.622% ± 4.644%
Expert 2 | 2.852% ± 2.252% | 28.604% ± 3.294% | 5.992% ± 2.719% | 31.46% ± 2.567%
Hybrid Expert | 0.599% ± 0.064% | 2.162% ± 1.69% | 9.007% ± 2.468% | 2.761% ± 1.705%
Calibrated Overkill, Leakage and Unknown rate on other datasets – 3 fruit
Appendix - Comparing the Performance between Expert 1, Expert 2, and Hybrid Expert
We separately evaluate the performance of Expert 1 and Expert 2, comparing them to our hybrid expert approach to understand the limitations of using only one of them.
The experimental results, averaged over three different dataset splits, utilized all fruit (old + new fruit).
The introduction of the dataset can be found on page 109.

## Slide 126
Normal
Anomaly
Appendix - The introduction of the dataset - MVtexAD
With different random seeds, a different texture will be selected as the new object.
The new object is then not using bad samples in the Defect Detector branch.
Upper branch of hybrid expert uses 5 texture. 4 of them has both good and bad(old object). 1 of them only has good samples (new object).
Lower branch of hybrid expert uses 5 texture. ALL of them only has good samples.

## Slide 127
Background : Training set
Foreground : Test set (Red circle and Green Cross )
Upper branch
(Defect detection)
Gaussian Process classifier
ties to
prediction
Uncertainty
Converter
prediction
Uncertainty
to defect
converter
Feature Extractor
Prediction
Combiner
MLP classifier
Expert 1 : use only the upper branch
Appendix
- t-sne visualization of z from train and test samples
Notes: In (a) Expert 1, the bad test samples overlap with the good test samples. In addition, missing and stand islands are mixed in the feature space
In (b) Expert 2, missing and stand islands are not mixed in the feature space.
The missing and stand islands are separated in (c) Hybrid Expert.
Furthermore, the bad test samples are push away from the good test samples as illustrated in (c) Hybrid Expert.

## Slide 128
Background : Training set
Foreground : Test set (Red circle and Green Cross )
(b) Lower branch
(Component classification)
Gaussian Process classifier
ties to
prediction
Uncertainty
Converter
prediction
Uncertainty
to defect
converter
Feature Extractor
Prediction
Combiner
MLP classifier
Expert 2 : use only the lower branch
Appendix
- t-sne visualization of z from train and test samples
Notes: In (a) Expert 1, the bad test samples overlap with the good test samples. In addition, missing and stand islands are mixed in the feature space
In (b) Expert 2, missing and stand islands are not mixed in the feature space.
The missing and stand islands are separated in (c) Hybrid Expert.
Furthermore, the bad test samples are push away from the good test samples as illustrated in (c) Hybrid Expert.

## Slide 129
Background : Training set
Foreground : Test set (Red circle and Green Cross )
Gaussian Process classifier
ties to
prediction
Uncertainty
Converter
prediction
Uncertainty
to defect
converter
Feature Extractor
Prediction
Combiner
MLP classifier
(c) Hybrid Expert
Hybrid Expert : Base on DUE
Appendix
- t-sne visualization of z from train and test samples
Notes: In (a) Expert 1, the bad test samples overlap with the good test samples. In addition, missing and stand islands are mixed in the feature space
In (b) Expert 2, missing and stand islands are not mixed in the feature space.
The missing and stand islands are separated in (c) Hybrid Expert.
Furthermore, the bad test samples are push away from the good test samples as illustrated in (c) Hybrid Expert.

## Slide 130
(b)
(a)
Note that only good samples of the training set are shown in the background.
Background : Training set
Foreground : Test set (Red circle and Green Cross )
Appendix - t-SNE visualization for previously proposed Hybrid Expert - MVtexAD

## Slide 131
(c) ArcFace Loss
(b) CosFace Loss
(a) Triplet Loss
Note that only good samples of the training set are shown in the background.
Background : Training set
Foreground : Test set (Red circle and Green Cross )
Appendix - t-SNE visualization of on other loss function - MVtexAD

## Slide 132
Method | Overkill rate | Leakage rate | Unknown rate | Overkill + Leakage rate | Score
GP is used in Stage 1 (k inducing point) No stage 2. | 3.27% ± 2.94% | 15.085% ± 5.076% | 39.56% ± 9.531% | 18.36% ± 2.471% | 0.8337
GP is used in Stage 1 (k inducing point) GMM is used in Stage 2 | 0% ± 0% | 18.987% ± 1.379% | 55.06% ± 9.886% | 18.99% ± 1.379% | 0.80122
GP is used in Stage 1 (k inducing point) GP is used in Stage 2 (k*50 inducing point) (Our Method) | 0.844% ± 1.462% | 16.245% ± 4.389% | 54.33% ± 10.35% | 17.09% ± 3.019% | 0.8091
Appendix - Comparison of the effect of (a) using GMM (b) using GP, in stage 2 and (c) without stage 2
Overkill, Leakage and Unknown rate on other datasets - MVtexAD
Of the experiments above, Stage 1 used Gaussian process classifier for fair comparison.
We will investigate the effects of employing different methods in Stage 2 of our approach.
The experimental results, averaged over three different dataset splits, utilized all object (old + new object).
The introduction of the dataset can be found on page 124.

## Slide 133
Method | Calibrated Overkill rate | Calibrated Leakage rate | Unknown rate | Calibrated Overkill + Leakage rate | Calibrated Score
GP is used in Stage 1 (k inducing point) No stage 2. | 4.953% ± 4.376% | 26.3% ± 12.86% | 39.56% ± 9.531% | 31.26% ± 8.646% | 0.7979
GP is used in Stage 1 (k inducing point) GMM is used in Stage 2 | 0% ± 0% | 43.34% ± 7.442% | 55.06% ± 9.886% | 43.34% ± 7.442% | 0.74162
GP is used in Stage 1 (k inducing point) GP is used in Stage 2 (k*50 inducing point) (Our Method) | 1.587% ± 2.75% | 37.568% ± 15.12% | 54.33% ± 10.35% | 38.65% ± 12.94% | 0.75333
Appendix - Comparison of the effect of (a) using GMM (b) using GP, in stage 2 and (c) without stage 2
Calibrated Overkill, Leakage and Unknown rate on other datasets - MVtexAD
Of the experiments above, Stage 1 used Gaussian process classifier for fair comparison.
We will investigate the effects of employing different methods in Stage 2 of our approach.
The experimental results, averaged over three different dataset splits, utilized all object (old + new object).
The introduction of the dataset can be found on page 124.

## Slide 134
Method | Overkill rate | Leakage rate | Unknown rate | Overkill + Leakage rate | Score
Triplet | 0% ± 0% | 13.61% ± 3.731% | 57.6% ± 8.222% | 13.61% ± 3.731% | 0.81165
CosFace | 0% ± 0% | 28.17% ± 4.138% | 50.95% ± 8.246% | 28.17% ± 4.138% | 0.78511
ArcFace | 0% ± 0% | 23.21% ± 6.284% | 58.02% ± 11.33% | 23.21% ± 6.284% | 0.78423
Multi-similarity | 0% ± 0% | 9.81% ± 2.759% | 55.17% ± 8.387% | 9.81% ± 2.759% | 0.82751
Our Method | 0.844% ± 1.462% | 16.245% ± 4.389% | 54.33% ± 10.35% | 17.09% ± 3.019% | 0.8091
Overkill, Leakage and Unknown rate on other datasets - MVtexAD
Appendix - Comparing the performance of different metric learning methods with previously proposed Hybrid Expert
The experimental results, averaged over three different dataset splits, utilized all object (old + new object).
The introduction of the dataset can be found on page 124.
We compared the performance of different metric learning methods used in the lower branch of the previously proposed Hybrid Expert.

## Slide 135
Method | Calibrated Overkill rate | Calibrated Leakage rate | Unknown rate | Calibrated Overkill + Leakage rate | Calibrated Score
Triplet | 0% ± 0% | 32.06% ± 6.26% | 57.6% ± 8.222% | 32.06% ± 6.26% | 0.76263
CosFace | 0% ± 0% | 57.59% ± 2.086% | 50.95% ± 8.246% | 57.59% ± 2.086% | 0.721
ArcFace | 0% ± 0% | 55.26% ± 0.372% | 58.02% ± 11.33% | 55.26% ± 0.372% | 0.71175
Multi-similarity | 0% ± 0% | 21.72% ± 2.695% | 55.17% ± 8.387% | 21.72% ± 2.695% | 0.79358
Our Method | 1.587% ± 2.75% | 37.568% ± 15.12% | 54.33% ± 10.35% | 38.65% ± 12.94% | 0.75333
Calibrated Overkill, Leakage and Unknown rate on other datasets - MVtexAD
Appendix - Comparing the performance of different metric learning methods with previously proposed Hybrid Expert
The experimental results, averaged over three different dataset splits, utilized all object (old + new object).
The introduction of the dataset can be found on page 124.
We compared the performance of different metric learning methods used in the lower branch of the previously proposed Hybrid Expert.

## Slide 136
Method | Overkill rate | Leakage rate | Unknown rate | Overkill + Leakage rate
Expert 1 | 17.3% ± 3.17% | 26.06% ± 2.154% | - | 43.35% ± 4.114%
Expert 2 | 1.16% ± 2.01% | 56.22% ± 2.154% | 0% ± 0% | 57.38% ± 0.483%
Hybrid Expert | 0.844% ± 1.462% | 16.245% ± 4.389% | 54.33% ± 10.35% | 17.09% ± 3.019%
Overkill, Leakage and Unknown rate on other datasets - MVtexAD
Appendix - Comparing the Performance between Expert 1, Expert 2, and Hybrid Expert
We separately evaluate the performance of Expert 1 and Expert 2, comparing them to our hybrid expert approach to understand the limitations of using only one of them.
The experimental results, averaged over three different dataset splits, utilized all object (old + new object).
The introduction of the dataset can be found on page 124.

## Slide 137
Method | Calibrated Overkill rate | Calibrated Leakage rate | Unknown rate | Calibrated Overkill + Leakage Rate
Expert 1 | 17.3% ± 3.17% | 26.06% ± 2.154% | - | 43.35% ± 4.114%
Expert 2 | 1.16% ± 2.01% | 56.22% ± 2.154% | 0% ± 0% | 57.38% ± 0.483%
Hybrid Expert | 1.587% ± 2.75% | 37.568% ± 15.12% | 54.33% ± 10.35% | 38.65% ± 12.94%
Calibrated Overkill, Leakage and Unknown rate on other datasets - MVtexAD
Appendix - Comparing the Performance between Expert 1, Expert 2, and Hybrid Expert
We separately evaluate the performance of Expert 1 and Expert 2, comparing them to our hybrid expert approach to understand the limitations of using only one of them.
The experimental results, averaged over three different dataset splits, utilized all object (old + new object).
The introduction of the dataset can be found on page 124.

## Slide 138
Appendix
- Validate the effectiveness of GP on classification tasks
CUB-200-2011
Method (Backbone : Resnet50 ) | classification Accuracy (%)
Triplet | 67.156 % ± 0.757 %
CosFace | 75.997 % ± 0.344 %
ArcFace | 75.318 % ± 0.123%
Multi-similarity | 69.183 % ± 0.374 %
GP is used Stage 1 | 75.412 % ± 0.582 %
GP is used Stage 1 and Stage 2 | 76.28 % ± 0.516 %

## Slide 139
Cifar-10
Method (Backbone : Resnet50 ) | classification Accuracy (%)
Triplet | 84.01 % ± 0.332 %
CosFace | 81.6 % ± 0.255 %
ArcFace | 80.22 % ± 0.516%
Multi-similarity | 83.91 % ± 0.326 %
GP is used Stage 1 | 88.67 % ± 0.029 %
GP is used Stage 1 and Stage 2 | 88.75 % ± 0.045 %
Appendix
- Validate the effectiveness of GP on classification tasks

## Slide 140
Cifar-100
Method (Backbone : Resnet50 ) | classification Accuracy (%)
Triplet | 83.66 % ± 0.357 %
CosFace | 81.55 % ± 0.245%
ArcFace | 80.4 % ± 0.705%
Multi-similarity | 83.48 % ± 0.506 %
GP is used Stage 1 | 88.24 % ± 0.722 %
GP is used Stage 1 and Stage 2 | 88.99 % ± 0.021 %
Appendix
- Validate the effectiveness of GP on classification tasks

## Slide 141
Flowers102
Method (Backbone : Resnet50 ) | classification Accuracy (%)
Triplet | 89.48 % ± 0.15 %
CosFace | 84.87 % ± 1.162%
ArcFace | 84.74 % ± 1.57%
Multi-similarity | 88.59 % ± 0.315 %
GP is used Stage 1 | 89.77 % ± 0.15 %
GP is used Stage 1 and Stage 2 | 90.95% ± 0.15%
Appendix
- Validate the effectiveness of GP on classification tasks